## Slide 1
City Wide Applications of WinSLAMM using the Batch Processor and Decision Analyses
Using WinSLAMM v10 to Meet Urban Stormwater Management Goals

## Slide 2: City-Wide WinSLAMM Application
Purpose:
Establish “Base” or “No Controls” Urban Pollution Loads
Analyze the Effect of Existing Stormwater Controls on the “Base” Load
Identify High Priority Areas to Focus Management
Determine Cost Effective Stormwater Control Practices

## Slide 3: City-Wide WinSLAMM Application
Example: Racine, WI
Challenge:
Population: 81,800
City Area: 16 square miles
Outfalls: 97
Subbasins: 245

## Slide 4: City-Wide WinSLAMM Application
Example: Racine, WI
Choice #1:
Create a “*.mdb” file for each of the 245 subbasins
Example of one subbasin:

## Slide 5: City-Wide WinSLAMM Application
Or…
swales
curb & gutter
sweep 1/wk
sweep 2/yr
sandy
clayey
Land Use

## Slide 6: City-Wide WinSLAMM Application
Choice #2:
Create Unit Area Loading Database with 4 variables:
Land use (26 combinations of LU & roof connections)
Soils (2)
Drainage Type (2)
Management Practices (15 combinations)
1,560 Potential Combinations

## Slide 7
Racine GIS
Example
Land Use
Coverage

## Slide 8
Racine GIS
Example
Soils
Coverage
(Hydrologic Groups)

## Slide 9
Racine GIS
Example
Land Use
Soils
Polygons of Combined Conditions
Drainage
Stormwater Controls

## Slide 10
Racine GIS Example: Results
Solids Load by Subbasin
Rank Subbasins
ID Priority Subbasins

## Slide 11
Racine GIS
Example
Identify “Critical” Subbasins

## Slide 12
Racine GIS
Example
ID Alternative Stormwater Control Practices

## Slide 13: Running a Set of *.mdb Files
Run a Series of WinSLAMM Data Files at One Time
View and Analyze the Results in Spreadsheet
Compare Files with Control Practices to a Base Conditions File
Analysis Cost Data
Notes: 1. To Run a Selected Series of .dat Files:
a. Select the folder that contains the files that you want to analyze by pressing the 'Select Directory' button. The .dat files in that directory will appear in the left-most list box on the window, as files listed in the current directory. In the list box immediately to the right is a list of the standard land use (SLU) type of each of the files. If the file is not a standard land use file, it will say 'Not a SLU File'.
b. Add the files you want to analyze to the Run List. To do this, either double click on individual files or press the 'Add All Listed Files to Run List' button.
c. Press the 'Run Files in Run List' button. This will run each of the files. This output can then be viewed and analyzed in Excel or by selecting the 'View Output File" button. This feature is especially useful when comparing different control practice alternatives for a site.

## Slide 14
Double-Click on Standard Land Use File to see Source Area Names and Areas in this Pane
Batch Editor

## Slide 15
View Source Area Name and Area (acres)
Batch Editor

## Slide 16: Running a Set of *.mdb Files
Or Select “Add All Files to Run List” to Run Them All
Double Click on a Specific File Name to Select one or More *.mdb Files

## Slide 17: Running a Set of *.mdb Files
View the Output in WinSLAMM or…
Notes: The output file will have the name 'DATSetOutput.csv' in the same directory as .dat files listed in the current directory. If you elected to evaluate the cost of the practices in your file, this file will also include the cost data for each file in your list. This file will be over-written if you run the files in the Run List again, so save the file with a different name if you want to save the output.

## Slide 18: Running a Set of *.mdb Files
Open the Output File in a Spreadsheet

## Slide 19
WinSLAMM Treatment Practices
Plus, we now have upflow filters and hydrodynamic devices, and are working on other media filters and combination controls

## Slide 20
WinSLAMM Summary Data Outputs
Runoff Volume (ft3, percent reduction; and Rv, runoff coefficient), particulate solids (lbs and mg/L), for:
- source area total without controls
- total before drainage system
- total after drainage system
total after outfall controls
Total control practice costs:
- capital costs
- land cost
- annual maintenance cost
- present value of all costs
annualized value of all costs
Receiving water impacts due to stormwater runoff:
- calculated Rv with and without controls
- approximate biological condition of receiving water (good, fair, or poor)
- flow duration curves (probabilities of flow rates for current model run and without controls)

## Slide 21
Detailed Data Outputs for Each Event
Runoff Volume (ft3), source area contributions, particulate solids (lbs and mg/L), pollutants (lbs and mg/L)
- by source area for each rain event
- land use total
- summary for all rains
- total for land use and for each event
- outfall summary, before and after drainage system and before and after outfall controls
- Rv (runoff volume only)
- total losses (runoff volume only)
- calculated CN (runoff volume only)

## Slide 22
The WinSLAMM batch editor can be used to automatically run a large number of files, usually for integration into a GIS-based map.

## Slide 23
File Name | Runoff Volume (cf) | Partic. Solids Yield (lbs) | Sub Basin Capital Cost | Sub Basin Land Cost | Sub Basin Maint. Cost | Sub Basin Total Annual Cost | Sub Basin Total Present Value Cost | % Part. Solids Reduc. | Cost per lb Sediment Reduced
Cost Example - Base Case No Controls | 5246545 | 37413 | 0 | 0 | 0 | 0 | 0 | 0% | n/a
Cost Example - G | 3136146 | 22341 | 119109 | 0 | 9100 | 18658 | 232515 | 40% | $ 1.24
Cost Example - P 20 percent | 4425257 | 30761 | 681686 | 0 | 3422 | 58122 | 724332 | 18% | $ 8.74
Cost Example - P 50 percent | 3193328 | 20784 | 1704215 | 0 | 8555 | 145306 | 1810829 | 44% | $ 8.74
WinSLAMM can also calculate life-cycle costs and compare different control programs to obtain unit removal costs with the batch processor:

## Slide 24: Decision Analysis
With so much data available, and so many options that can be analyzed, how does one select the “best” stormwater control program?
The least costly that meets the objective?

## Slide 25
Possible, if only have one numeric standard:
If 80% SS reduction goal, the least costly would be wet detention. In this example, grass swales, street cleaning, and catchbasins cannot reach this level of control. If 40% SS reduction goal, then grass swales wins.

## Slide 26
If multiple goals, then possibly not as clear and need a more flexible approach. Consider the following example (a conservation design industrial park in Huntsville, AL):

## Slide 27
This site was divided into four subareas, one area has 13 industrial lots (about 2.6 acres each), plus a large undeveloped area (60.2 acres) and isolated sinkholes (4.6 acres). The developed area is divided into the following:
• Roofs plus paved parking: 20.7 acres
• Streets (1.27 curb-miles): 3.1 acres
• Small landscaped areas (B, or sandy-loam soils, but
assumed silty soils due to compaction): 10.0 acres
Conventional drainage system costs (5% over 20 yrs) were estimated to be:
Capital cost of project = $296,400 (2005)
Annual maintenance cost = $2,960/year (2005)
Annual cost of conventional drainage = $26,850 per year

## Slide 28
Biofilters to drain site runoff (paved parking and roofs) to regional swales:
Top area: 4400 ft2
Bottom area: 2000 ft2
Depth: 2 ft
Seepage rate: 2 in/hr
Peak to average flow ratio: 3.8
Typical width: 10 ft
Number of biofilters: 13 (one per site)
Parking lot biofilter example, Portland, OR

## Slide 29
Regional swales to
collect site runoff and direct to wet detention ponds:
Length: 1653 ft
infiltration rate in the swale:
1 in/hr
swale bottom width: 50 ft
3H:1V side slopes
longitudinal slope: 0.026 ft/ft
Manning’s n roughness coefficient: 0.024
typical swale depth: 1 ft
WI swale having conventional curbs and gutters
Large swale at MS industrial site

## Slide 30
Pond Elevation (ft) | Full-Sized Pond Area (acres)
1 | 0.15
2 | 0.25
3 | 0.5
4 | 0.75
5 | 1.0 (normal pool elevation, and invert elevation of 30o v-notch weir)
6 | 1.5
7 | 2
8 | 2.5 (invert elevation of flood flow broad-crested weir). Normal maximum elevation during one and two year rains.
9 | 3.0 (approximate maximum pond elevation, or as determined based on flood flow analysis). Additional storage and emergency spillway may be needed to accommodate flows in excess of the design flood flow.
Wet Detention Pond to Treat Runoff from Area

## Slide 31
Stormwater Treatment Option | Annual Total SW Treat. Cost ($/yr) | Annual Addit. Drain. System Cost ($/yr) | Total Annual Cost ($/yr) | Land Needs for SW mgt (acres) | Runoff Volume (cf/yr) | Part. Solids Yield (lbs/yr) | Reduc. in SS Yield (%)
Base, No Controls | 0 | 64,230 | 64,230 | 0 | 5,600,000 | 71,375 | n/a
Option 1 Pond | 19,134 | 64,230 | 83,364 | 4.5 | 5,507,000 | 10,192 | 86
Option 2 Reg. Swale | 3,158 | 26,850 | 30,008 | 0 | 2,926,000 | 32,231 | 55
Option 3 Site Biofilter | 32,330 | 37,380 | 69,710 | 0 | 2,705,000 | 68,890 | 1
Option 4 Small pond | 10,209 | 64,230 | 74,439 | 2.3 | 5,557,000 | 19,552 | 73
Option 5 Pond and reg. swale | 22,292 | 26,850 | 49,142 | 4.5 | 2,844,000 | 4,133 | 94
Option 6 Pond, swale, biofilter | 54,622 | 0 | 54,622 | 4.5 | 1,203,000 | 2,183 | 97
Option 7 Small pond and swale | 13,367 | 26,850 | 40,217 | 2.3 | 2,887,000 | 6,937 | 90
Option 8 Small pond, swale and biofilter | 45,698 | 0 | 45,698 | 2.3 | 1,253,000 | 4,125 | 94
Batch Processor Data for Combinations of Above Controls

## Slide 32
Stormwater Treatment Option | Part. Phos Yield (lbs/yr) | Volum. Runoff Coeff. (Rv) (est. bio. cond.) | % of time flow >1 cfs | % of time flow >10 cfs | SS conc. (mg/L) | Part. P conc. (mg/L) | Zn conc. (µg/L)
Base, No Controls | 174 | 0.29 (poor) | 4.5 | 0.3 | 204 | 0.50 | 359
Option 1 Pond | 25 | 0.29 (poor) | 4 | 0.05 | 30 | 0.073 | 128
Option 2 Reg. Swale | 79 | 0.15 (fair) | 2 | 0.1 | 178 | 0.43 | 390
Option 3 Site Biofilter | 172 | 0.14 (fair) | 2 | 0.2 | 408 | 1.0 | 696
Option 4 Small pond | 41 | 0.29 (poor) | 4 | 0.2 | 48 | 0.12 | 151
Option 5 Pond and reg. swale | 10 | 0.15 (fair) | 2 | 0 | 23 | 0.057 | 203
Option 6 Pond, swale, biofilter | 5.5 | 0.06 (good) | 0.5 | 0 | 29 | 0.073 | 386
Option 7 Small pond and swale | 17 | 0.15 (fair) | 2 | 0.05 | 39 | 0.095 | 220
Option 8 Small pond, swale and biofilter | 10 | 0.07 (good) | 0.8 | 0 | 53 | 0.13 | 390
Additional Batch Processor Data (cont.)

## Slide 33
Specific criteria or limits that must be met.
It is possible to simply filter out (remove) the options that do not meet all of the absolutely required criteria. If the options remaining are too few, or otherwise not very satisfying, continue to explore additional options. The above examples only considered combinations of 3 types of stormwater control devices, for example. There are many others that can also be explored. If the options that meet the absolute criteria look interesting and encouraging, then continue.
Decision Analysis Approaches

## Slide 34
Stormwater Treatment Option | Total Annual Cost ($/yr) | Reduction in SS Yield (%) | Meet 80% particulate solids reduction goal? | Rank based on annual cost
Option 1 Pond | 83,364 | 86 | Yes | 5
Option 2 Regional Swale | 30,008 | 55 | No | n/a
Option 3 Site Biofilter | 69,710 | 1 | No | n/a
Option 4 Half-sized pond | 74,439 | 73 | No | n/a
Option 5 Pond and reg. swale | 49,142 | 94 | Yes | 3
Option 6 Pond, reg. swale and biofilter | 54,622 | 97 | Yes | 4
Option 7 Small pond and reg. swale | 40,217 | 90 | Yes | 1
Option 8 Small pond, reg. swale and biofilter | 45,698 | 94 | Yes | 2
Control Options Meeting 80% SS Reduction Requirement, Ranked by Cost

## Slide 35
2) Goals that are not absolute (based on methods developed by Keeney, R.L. and H. Raiffa. 1976. Decision Analysis with Multiple Conflicting Objectives. John Wiley & Sons. New York.)
Utility curves and tradeoffs can be developed for the remaining attributes, after all the absolutely required goals are met. The above example includes attributes of several different types:
- costs
- land requirements
- runoff volume (volumes, habitat responses, and
rates)
- particulate solids (reductions, yields and
concentrations)
- particulate phosphorus (reductions, yields and
concentrations)
- total zinc (reductions, yields and concentrations)

## Slide 36
Attribute | Range of attribute value for acceptable options | Attribute ranks for selection (after absolute goals are met) | Trade-offs between remaining attributes
Total annual cost ($/year) | $40,217 to 83,364 | 2 | 0.20
Land needs (acres) | 2.3 to 4.5 acres | 5 | 0.08
Rv | 0.06 to 0.29 | 1 | 0.30
% of time flow >1 cfs | 0.5 to 4 % | 7 | 0.05
% of time flow >10 cfs | 0 to 0.05 % | 3 | 0.18
Particulate solids yield (lbs/yr) | 2,183 to 10,192 lbs/yr | 6 | 0.07
Part. Phosphorus yield (lbs/yr) | 5.5 to 25 lbs/yr | 4 | 0.12
 |  |  | Sum = 1.0
Attribute Value Ranges, plus Example Ranks and Trade-offs (ranks and trade-offs could vary for different interested parties)

## Slide 37
• Volumetric runoff coefficient (Rv) as an indicator of habitat quality and aquatic biology stress:
Attribute Expected Utility
Value Habitat Value
Condition
<0.1 Good 1.0
0.1 to 0.25 Fair 0.75
0.26 to 0.50 Poor 0.25
0.51 to 1.0 Really lousy 0
Utility Curves for Different Attributes (technically based, would not vary for different interested parties)

## Slide 38
Notes: This a classical example of steam degradation
0-10% impervious cover---there are excellent conditions in streams
It has been found that there are 2 thresholds in stream degradations:
      At ~low levels of imperviousness (10-15%) when stream degradation occurs
      At 25-30% imperviousness significant degradations is already observed (damaged)
Those thresholds are similar with the point on the curve (17 land uses, 43 years of rain, long term averages, assuming sandy and clayly conditions)
This graph illustrate the relationships between the directly connected impervious area percentages and the calculated volumetric runoff coefficients (Rv) for each land use category (using the average land use characteristics), based on 43 years of local rain data.
Rv is relatively constant until the 10 to 15% impervious cover values are reached (at Rv = 0.07 for sandy soil areas and 0.16 for clayey soil areas), the point where receiving water degradation typically is observed to start
The 25 to 30% impervious levels (where significant degradation is observed), is associated with Rv values of about 0.14 for sandy soil areas and 0.25 for clayey soil areas, and is where the curves start to greatly increase in slope.

## Slide 39
• Part. Phosphorus yield (lbs/yr): straight line, with 25 lbs/yr = 0 and 5.5 lbs/yr = 1.0
• Land needs (acres): straight line, with 4.5 acres = 0 and 2.3 acres = 1.0
• Particulate solids yield (lbs/yr): straight line, with 10,192 lbs/yr = 0 and 2,183 lbs/yr = 1.0
• % of time flow >1 cfs Utility value
<1 1.0
1 – 3 0.75
3.1 – 10 0.25
>10 0
Example Utility Values for Other Attributes (cont):

## Slide 40
Stormwater Control Option | Total Annual Cost ($/yr) | Cost utility | Land Needs for SW mgt (acres) | Land utility | Part. Solids Yield (lbs/yr) | Part. Solids utility | Part. Phos. Yield (lbs/yr) | Phos. utility
Tradeoff Value |  | 0.20 |  | 0.08 |  | 0.07 |  | 0.12
Option 1 Pond | 83,364 | 0 | 4.5 | 0 | 10,192 | 0 | 25 | 0
Option 5 Pond and reg. swale | 49,142 | 0.79 | 4.5 | 0 | 4,133 | 0.76 | 10 | 0.77
Option 6 Pond, reg. swale and biofilter | 54,622 | 0.67 | 4.5 | 0 | 2,183 | 1.0 | 5.5 | 1.0
Option 7 Small pond and reg. swale | 40,217 | 1 | 2.3 | 1 | 6,937 | 0.41 | 17 | 0.41
Option 8 Small pond, reg. swale and biofilter | 45,698 | 0.87 | 2.3 | 1 | 4,125 | 0.76 | 10 | 0.77
Attribute Values and Associated Utilities for Example

## Slide 41
Stormwater Control Option | Volumetric Runoff Coefficient (Rv) | Rv utility | % of time flow >1 cfs | Mod flow utility | % of time flow >10 cfs | High flow utility
Tradeoff Value |  | 0.30 |  | 0.05 |  | 0.18
Option 1 Pond | 0.29 | 0.25 | 4 | 0.25 | 0.05 | 0.75
Option 5 Pond and reg. swale | 0.15 | 0.75 | 2 | 0.75 | 0 | 1.0
Option 6 Pond, reg. swale and biofilter | 0.06 | 1.0 | 0.5 | 1.0 | 0 | 1.0
Option 7 Small pond and reg. swale | 0.15 | 0.75 | 2 | 0.75 | 0.05 | 0.75
Option 8 Small pond, reg. swale and biofilter | 0.07 | 1.0 | 0.8 | 1.0 | 0 | 1.0
Attribute Values and Associated Utilities for Example (cont.)

## Slide 42
Stormwater Control Option | Cost utility | Cost factor | Land utility | Land factor | Part. utility | Part. factor | Phos. utility | Phos factor
Tradeoff Value | 0.20 |  | 0.08 |  | 0.07 |  | 0.12 | 
Option 1 Pond | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Option 5 Pond and reg. swale | 0.79 | 0.158 | 0 | 0 | 0.76 | 0.053 | 0.77 | 0.092
Option 6 Pond, reg. swale and biofilter | 0.67 | 0.134 | 0 | 0 | 1.0 | 0.07 | 1.0 | 0.12
Option 7 Small pond and reg. swale | 1 | 0.20 | 1 | 0.08 | 0.41 | 0.029 | 0.41 | 0.049
Option 8 Small pond, reg. swale and biofilter | 0.87 | 0.174 | 1 | 0.08 | 0.76 | 0.053 | 0.77 | 0.092
Calculation of Factors for Each Option
(Attribute Utility times Attribute Trade-off)

## Slide 43
Stormwater Control Option | Rv utility | Rv factor | Mod flow utility | Mod flow factor | High flow utility | High flow factor | Sum of factors | Over-all Rank
Tradeoff Value | 0.30 |  | 0.05 |  | 0.18 |  |  | 
Option 1 Pond | 0.25 | 0.075 | 0.25 | 0.0125 | 0.75 | 0.135 | 0.2225 | 5
Option 5 Pond and reg. swale | 0.75 | 0.225 | 0.75 | 0.0375 | 1.0 | 0.18 | 0.7455 | 4
Option 6 Pond, reg. swale and biofilter | 1.0 | 0.30 | 1.0 | 0.05 | 1.0 | 0.18 | 0.8540 | 2
Option 7 Small pond and reg. swale | 0.75 | 0.225 | 0.75 | 0.0375 | 0.75 | 0.135 | 0.7555 | 3
Option 8 Small pond, reg. swale and biofilter | 1.0 | 0.30 | 1.0 | 0.05 | 1.0 | 0.18 | 0.9290 | 1
Calculation of Factors for Each Option (cont.), Sum of Factors, and Overall Rank

## Slide 44: Conclusions
Calibrated and verified stormwater models can be used to develop a great deal of information concerning many different stormwater management options.
Regulations and criteria also need to have different formats to acknowledge site specific problems and objectives.
The use of clear and flexible decision analysis techniques is therefore important when selecting the most appropriate stormwater control program for a site.