## Slide 1: WinSLAMM v 10 Routing of Particle Size Distributions
Using WinSLAMM v10 to Meet Urban Stormwater Management Goals

## Slide 2: Routing of Particle Size Distributions (PSD) in WinSLAMM
The newest version of WinSLAMM can assign PSDs to source areas.
The PSDs are then routed throughout the drainage system, including the control practices.
This is a great improvement as it offers maximum flexibility when adding or editing stormwater control practices by allowing the program to automatically calculate the influent PSD for all conditions, instead of requiring the model user to select the PSD manually for the first control in a series.

## Slide 3: One of the Most Important New Features of WinSLAMM Version 10 is its’ Ability to Route Hydrographs and Particle Size Distributions through Successive Control Practices
Upgradient hydrograph modifications usually improve the performance of downgradient controls mostly due to decreased peak treatment flow rates.
Particle size distribution routing through control practices provides more accurate overall performance calculations (e.g., errors associated with double counting due to removal of larger particles removed by preceding controls).
These enhancements result in an improved ability to accurately model treatment trains and to select and size complementary control practices throughout an area.

## Slide 4
100 acre Institutional Area Hydrograph and particle size routing through string of five wet detention ponds, each increasing in area downgradient.
 | area at lowest invert, at 4 ft. stage (ac) | max pond surface area (ac)
pond 1 | 0.20 | 0.50
pond 2 | 0.30 | 0.75
pond 3 | 0.50 | 1.25
pond 4 | 0.90 | 1.50
pond 5 | 1.65 | 2.75

## Slide 10
Particle Size Distribution effluent calculation procedure uses mass-weighting rather than flow-weighting

## Slide 15: TSS vs. SSC and PSD Relationships
Two separate issues:
  sampling to obtain representative water samples and
  laboratory processing to represent all particles.
  Most problems result in loss of large particles. The combination of methods used affects modeling approach, especially the particle size distributions.

## Slide 16: Sampling Effects on Particulate Solids Characteristics
Sampling issues associated with stratified flows and bedload.
  Sampler intakes on bottom of pipe may collect more bedload than represented in well-mixed sample, and
  sampler tube velocity may not be able to transport large particles to sample bottles
  These are two opposite problems that seldom cancel each other out nicely.

## Slide 17
Sampled solids load in | 1623 kg
Sampled solids load out | 1218 kg
Trapped by difference | 405 kg (25% removal)
Actual trapped total sediment | 536 kg (33% actual removal)
Fraction total solids not captured by automatic samplers | 8% (131 kg missed by sampler, out of 1623 kg in sampler)
Results of Verification Monitoring of Stormceptor (Madison, WI)
Standard automatic water samplers with single intakes at bottom of pipes. Influent samplers are affected by large particles while effluent samplers should not be, assuming the stormwater control is capable of removing the larger particles that stress the samplers.

## Slide 18
Bed load in storm drainage compromised about 4% of Madison area total solids discharges (WI DNR and USGS) monitoring).

## Slide 19
Bedload in corrugated stormdrain and mound of settleable material at discharge into wet detention pond after many years of operation at ski resort at Snowmass, CO (drain from several acre resort parking area having sand applications for traction control).

## Slide 20
Simple methods to obtain representative sample: create cascading and well-mixed flow at sampling location (well-mixed flow with bedload and no stratification). Examples shown for gutter and pipe flow installations.

## Slide 21
Depth integrated sampler developed by USGS to automatically collected samples at varying depths of flow.

## Slide 22
EPA TSS 160.2 Shake sample bottle vigorously then pour aliquot into graduated cylinder | Standard Methods TSS 2540D Use stir plate and pipet at mid-depth in bottle and midway between wall and vortex | USGS SSC D3977-97B Use entire sample and pour from original bottle
Comparison of Three TSS/SSC Analytical Methods

## Slide 23
USGS/Dekaport cone splitter used to separate sample into smaller volumes for different analyses.

## Slide 24
Chart: TSS (shake and pour vs. sitr and pipette)
| 92 | 566 | 463 | 69 | 83 | 168 | 96 | 56 | 25 | 68 | 3 | 29 | 53 | 62 | 173 | 48 | 28 | 48 | 28 | 504 | 252 | 795 | 93 | 126 | 273 | 86 | 128 | 150 | 129 | 212 | 131 | 46 | 68 | 103 | 93 | 58 | 77 | 136 | 204 | 60 | 55 | 24 | 44 | 269 | 165 | 119 | 173 | 202 | 59 | 51 | 83 | 63 | 86 | 107 | 43 | 133 | 64 | 86 | 123
TSS (sitr and pipette) | 127 | 698 | 528 | 83 | 98 | 179 | 118 | 66 | 32 | 89 | 3 | 33 | 66 | 98 | 262 | 72 | 31 | 52 | 35 | 571 | 274 | 1012 | 108 | 149 | 312 | 108 | 174 | 184 | 137 | 336 | 118 | 57 | 73 | 112 | 83 | 54 | 80 | 160 | 262 | 86 | 64 | 32 | 51 | 432 | 184 | 148 | 192 | 231 | 49 | 51 | 146 | 70 | 124 | 96 | 41 | 139 | 70 | 97 | 115
Chart: Shake and pour TSS vs. SSC
| 92 | 566 | 463 | 69 | 83 | 168 | 96 | 56 | 25 | 68 | 3 | 29 | 53 | 62 | 173 | 48 | 28 | 48 | 28 | 504 | 252 | 795 | 93 | 126 | 273 | 86 | 128 | 150 | 129 | 212 | 131 | 46 | 68 | 103 | 93 | 58 | 77 | 136 | 204 | 60 | 55 | 24 | 44 | 269 | 165 | 119 | 173 | 202 | 59 | 51 | 83 | 63 | 86 | 107 | 43 | 133 | 64 | 86 | 123
SSC | 124 | 693 | 543 | 88 | 102 | 180 | 121 | 67 | 26 | 92 | 3 | 41 | 60 | 111 | 257 | 68 | 32 | 51 | 28 | 630 | 348 | 711 | 94 | 141 | 306 | 95 | 193 | 403 | 140 | 319 | 64 | 54 | 62 | 64 | 90 | 60 | 81 | 153 | 246 | 62 | 63 | 50 | 52 | 412 | 176 | 130 | 195 | 204 | 50 | 50 | 204 | 75 | 79 | 125 | 45 | 171 | 84 | 89 | 86
shake and pour vs. stir and pipette |  | 
t-Test: Paired Two Sample for Means |  | 
 | Variable 1 | Variable 2
Mean | 132.7288 | 160.2034
Variance | 19818.3 | 31015.65
Observations | 59 | 59
Pearson Correlation | 0.989092 | 
Hypothesized Mean Difference | 0 | 
df | 58 | 
t Stat | -4.98885 | 
P(T<=t) one-tail | 2.92E-06 | 
shake and pour TSS vs. SSC |  | 
t-Test: Paired Two Sample for Means |  | 
 | Variable 1 | Variable 2
Mean | 132.7288 | 158.3559
Variance | 19818.3 | 26095.68
Observations | 59 | 59
Pearson Correlation | 0.949183 | 
Hypothesized Mean Difference | 0 | 
df | 58 | 
t Stat | -3.75887 | 
P(T<=t) one-tail | 0.000199 | 

## Slide 25
Chart: stir and pipette TSS vs. SSC
| 127 | 698 | 528 | 83 | 98 | 179 | 118 | 66 | 32 | 89 | 3 | 33 | 66 | 98 | 262 | 72 | 31 | 52 | 35 | 571 | 274 | 1012 | 108 | 149 | 312 | 108 | 174 | 184 | 137 | 336 | 118 | 57 | 73 | 112 | 83 | 54 | 80 | 160 | 262 | 86 | 64 | 32 | 51 | 432 | 184 | 148 | 192 | 231 | 49 | 51 | 146 | 70 | 124 | 96 | 41 | 139 | 70 | 97 | 115
SSC | 124 | 693 | 543 | 88 | 102 | 180 | 121 | 67 | 26 | 92 | 3 | 41 | 60 | 111 | 257 | 68 | 32 | 51 | 28 | 630 | 348 | 711 | 94 | 141 | 306 | 95 | 193 | 403 | 140 | 319 | 64 | 54 | 62 | 64 | 90 | 60 | 81 | 153 | 246 | 62 | 63 | 50 | 52 | 412 | 176 | 130 | 195 | 204 | 50 | 50 | 204 | 75 | 79 | 125 | 45 | 171 | 84 | 89 | 86
stir and pipette TSS vs. SSC |  | 
t-Test: Paired Two Sample for Means |  | 
 | Variable 1 | Variable 2
Mean | 160.2034 | 158.3559
Variance | 31015.65 | 26095.68
Observations | 59 | 59
Pearson Correlation | 0.953514 | 
Hypothesized Mean Difference | 0 | 
df | 58 | 
t Stat | 0.265473 | 
P(T<=t) one-tail | 0.395793 | 

## Slide 26: Sample Processing before Coulter Counter Analyses
The Coulter Counter Multi-Sizer 3 is most suitable for particles in the range of about 1 to 200 µm.
Larger particles (especially those of about 500 µm and larger) settle to the bottom of the measurement vessel and are not kept suspended and drawn through the analytical aperture.
Coulter recommends increasing the viscosity of the analytical solution (such as by using Karo syrup) to keep particles as large as 1,200 µm suspended. We were never pleased with this option.

## Slide 27
Coulter Counter Multi-Sizer 3 used to measure particle size distribution of solids up to several hundred micrometers. Larger particles (up to several mm) are quantified using sieves.

## Slide 28
Normally, we have found only a few “sand” grains in the bottom of sample bottles, or in the Coulter vessel, when the instrument was not recording their presence. We were not concerned due to their few number and minimal affect on sample mass.
During the past several years, we have started to separate the samples into at least three size fractions: >106, 0.45 to 106, and <0.45 µm. Generally, we divide the “suspended solids” fraction at 106.
The intermediate fraction was therefore used in the Coulter Counter analyses, with no possible interference with large particles. The relatively small fraction of particles >106 µm are therefore quantified and added to the size distribution (as is the <0.45 µm “dissolved” fraction).

## Slide 29
Before
After
Large particles (sands) are captured
in 106 micrometer sieve
Pre-sieving a sample with 106
micrometer sieve (before use of 140
micrometer aperture tube)
Sediment sample

## Slide 30
The sample is split using the cone splitter into 4 separate 100 mL subsamples (or more subsamples, as additional analyses are also being conducted).
One sample is analyzed for total solids (un-filtered), another sample is analyzed for dissolved solids (after filtering with a 0.45 µm membrane filter), and another sample is analyzed for total solids after passing through a 106 µm sieve. The fourth sample is analyzed in the Coulter Counter, after sieving through the same 106 µm sieve.

## Slide 31
Pre-sieving a sample with 20 micrometer sieve (before use of 32 micrometer aperture tube)

## Slide 32
Before
Pre-Sieving
Sieve
Large particles
After
Pre-Sieving
Coulter Counter analysis
Particles go through the hole in an aperture tube.
Particles in a sample must be smaller than the
diameter of the aperture tube.
Particles
Sample &
Electrolyte

## Slide 33
Sieving with a 106 µm sieve to remove large debris before Coulter counting. Similar sample analyzed for total solids.
Screened material showing grass debris (from 5L of sample)

## Slide 34
All-plastic vacuum filtering setups are used with a series of polycarbonate membrane filters (10, 5, 2, 1, 0.45µm). The filtrates are then chemically analyzed.

## Slide 35
Roof runoff particle size distributions (for TSS shake and pour on left and for TSS stir and pipette and SSC on right)

## Slide 36
Paved parking, storage, loading dock, vehicle service area, and street runoff particle size distributions (for shake and pour TSS on left and for stir and pipette TSS and SSC on right)

## Slide 37
Non-paved parking and storage area runoff particle size distributions (for shake and pour TSS on left; no stir and pipette or SSC data available)

## Slide 38
Landscaped, open space, and construction site runoff particle size distributions (for shake and pour TSS on left and for stir and pipette TSS and SSC on right)

## Slide 39
Outfall discharges particle size distributions (for shake and pour TSS on left and for stir and pipette TSS and SSC on right)
Note the relatively little differences in the PSDs at the outfalls for the two sample categories.

## Slide 40
Average particle size distributions for different source area categories (for shake and pour TSS on left and for stir and pipette and SSC on right)

## Slide 41
A new psd source area csv file is now used to identify which psd files are associated with each source area by land use