## Slide 1: Street Cleaning in WinSLAMM
Using WinSLAMM v10 to Meet Urban Stormwater Management Goals

## Slide 2: We will cover . . .
Research Results
How model calculates water quality benefits of street cleaning
Typical model output for street cleaning

## Slide 3
Street and catchbasin cleaning, and inlet controls most effective for smaller rains or heavily paved areas.

## Slide 5: Redistribution of Street Dirt During Street Cleaning
Pitt 1985

## Slide 6: Street Dirt Chemical Quality (mg/kg) (Milwaukee, WI; San Jose, CA; Bellevue, WA; Toronto, Canada; Reno, NV; Champaign, IL)
Phosphorus (P) | 400 – 1500
Total Kjeldahl Nitrogen | 290 – 4300
Chemical Oxygen Demand | 65,000 – 340,000
Copper (Cu) | 110 – 420
Lead (Pb) | 530 – 7500
Zinc (Zn) | 260 – 1200
Cadmium (Cd) | <3 – 5
Chromium (Cr) | 31 – 180
Pitt, Bannerman, and others

## Slide 7: Sawtooth Pattern Associated with Deposition and Removal of Particulates
Pitt 1979

## Slide 9
Pitt 1987
Washoff Plots for Heavy Rain Intensities, Dirty Streets,
and Rough Pavement Textures

## Slide 11: Total Particulate Loading , Keyes – Good Asphalt Test Area
Pitt 1979

## Slide 12: Total Solids Accumulation Since Last Cleaning
Pitt 1979

## Slide 13: Deposition and Accumulation of Street Dirt
Pitt 1979

## Slide 14: Total Solids Removal by Street Cleaning
Pitt 1979

## Slide 15: Washoff of Street Dirt, Bellevue, WA
Pitt 1985

## Slide 16: Goals of Studies
Collect Information to Predict Water Quality Benefits of Street Cleaning
  Pick-up efficiency
  Accumulation Rate of Street Dirt
  Wash-off of Street dirt during event
Water Quality Benefits at the End of the Pipe.

## Slide 17
High-Frequency Broom
Low-Frequency Broom
Control
Air Sweeper

## Slide 19: WATER QUALITY
Probe for Flow
Sample Intake

## Slide 20: Example of Water Samples Collected From Residential Storm Sewers

## Slide 21: Expected Change in Relationship Between Control and Test Site Pollutant Loads
No Street Cleaning
With Street Cleaning

## Slide 23
Other Sources (Wash On)
Delivery in Pipe
Factors Affecting Effectiveness of Street Cleaning

## Slide 24
Before Broom Street Cleaner
After Broom Street Cleaner

## Slide 25: Models Estimate Sawtooth Pattern Based on Street Load Data
Accumulation
Street Cleaning
Wash Off
Wash Off
Street Cleaning
Accumulation

## Slide 26
Street Loads Measured Before and After Every Cleaning; over time; and before and after rain
Measure Changes in Street Dirt Loads with Vacuum Cleaners – 2 Tons

## Slide 27: Average Percent Reduction in Street Dirt by Particle Size
Vacuum Assisted
Broom
Reg. Air

## Slide 28
Street Cleaning Effectiveness Reduced Because Gutter Broom Makes More Fine Particles Available for Wash Off

## Slide 29: Accumulation Functions

## Slide 30
Residential – 15 lbs\curb mile\day;
0.75 of Previous Interval after 15 days

## Slide 31: Total Solids Accumulation Since Last Cleaning
Pitt 1979

## Slide 32: Wash –off Functions

## Slide 33: Washoff of Street Dirt, Bellevue, WA
Pitt 1985

## Slide 34: Wash Off Coefficients for Smooth and Intermediate Streets
Street Load, lbs\curb mile | Rain Intensity of 3 mm\hr. (0.12 in\hr) | Rain Intensity of 12 mm\hr. (0.47 in\hr)
1400 | 0.20 | 0.26
400 | 0.15 | 0.35

## Slide 36: Productivity Functions

## Slide 37
Productivity Curve for Broom Cleaner
Y = 0.55X + 310 Residential, Intermediate Texture; Light Parking; No controls
No Change

## Slide 38
Productivity Curve for Vacuum Assisted Cleaner
No Change
Y = 0.70 X + 55
Residential; Intermediate;
Light Parking; No controls

## Slide 40: Variables in Street Cleaning Analysis
User Select:
Frequency
Parking Density
Parking Controls
Machine Type
Pre-Determined:
Winter Load
Rainfall File
Street Texture
Land Use

## Slide 41
Street Cleaning Form
Street Cleaning Dates and Frequency
Notes: The street cleaning control option can be applied to streets and alleys in land uses 1 through 5. No more than ten street cleaning schedule changes are allowed for each street or alley source area. Below is a description of the information requirements necessary to implement street cleaning.
Street cleaning starting date (date format: MM/DD/YY).
Street cleaning ending date (date format: MM/DD/YY).
Street cleaning schedule. The cleaning options are listed below:
1. None 2. 7 Passes/week
3. All weekdays (Mon-Fri) 4. 4 Passes/week (Mon,Tue,Thur,Fri
5. 3 Passes/week (Mon,Wed,Fri) 6. 2 Passes/week (Tue,Thur)
7. 1 Pass/week (Wed) 8. Every 2 weeks (Wed)
9. Every 4 weeks (Wed) 10. Every 8 weeks (Wed)
11. Every 12 weeks (Wed)

## Slide 42
Street Cleaning Form
Street Cleaner Productivity
Parking Conditions
Type of Street Cleaner
Notes: Street cleaning productivity. Select the default productivity by entering the parking density and the parking control status. The parking density options are:
1. None
2. Light
3. Medium
4. Extensive (short term)
5. Extensive (long term)
The parking control status indicates whether parking options such as limited parking hours or alternate side-of-the-street parking have been regulated by the municipality. If they have, select the "YES" button to indicate that parking controls are imposed.
Street sweeper productivity can also be described by entering the equation coefficients for the linear street cleaning equation, Y = mx + b, where is Y is the residual street dirt loading after street cleaning and x is the before street cleaning load (in lbs/curb-mile). Enter values for:
m (slope, less than 1)
b (intercept, greater than or equal to 1)
Where m is the minimum removal fraction, or street cleaning effectiveness, and b is the minimum street dirt loading, after intensive street cleaning.

## Slide 43: Effect of Cleaning Frequency on Annual TSS Reduction in Medium Density Residential
Cleaning Frequency | Broom Street Cleaner |  | Vacuum Assisted Street Cleaner | 
 | Light Parking | Medium Parking | Light Parking | Medium Parking
March & April – 1\Week | 5 | 3 | 5 | 5
1 \ 4 Weeks | 3 | 1 | 6 | 2
1 \ Week | 8 | 4 | 18 | 9

## Slide 44: Adding Highway Street Cleaning to WinSLAMM and Improving Method for Estimating Pollutant Concentrations for Highways.
Routines Calibrated included Runoff from Highway and Pervious Areas, Washoff, Accumulation, End of Pipe Loads, and Street Sweeping

## Slide 45: Evaluate Application of SLAMM to Street Cleaning on Highways

## Slide 46: Wisconsin DOT Study on East Washington, Madison
Vacuum before and after street cleaning – productive function
Vacuum for accumulation and washoff
Water quality site with no cleaning
Vacuum assisted machine

## Slide 47: Measuring Change in Street Dirt Load on East Washington

## Slide 48
Chart: Measured versus Modeled Sampled Runoff Volume at the End of Pipe
| 4095 | 5512 | 1054.0800000000002 | 7413.12 | 4224.96 | 1356.4799999999998 | 7845.1200000000008 | 3629 | 786.24 | 3214.08 | 1909 | 3153.6 | 8131 | 864 | 1002.2399999999999 | 8856 | 4700.16 | 6791 | 959.04000000000008 | 1304.6400000000001 | 959.04000000000008 | 1244.1599999999999 | 587.52 | 2540 | 4121.28 | 3153.6 | 2704.32 | 8976.9600000000009 | 1676.16 | 1831.68 | 2246.7200000000003 | 838.08 | 1175 | 3871 | 1563.8400000000001 | 4121.28 | 5978.88 | 4311.3599999999997 | 1823 | 4043.52 | 14618.900000000001 | 535.67999999999995 | 5780.16 | 7421.76 | 13236.48 | 2073.6 | 8683.2000000000007 | 7871 | 1019.52 | 2989.44 | 388.79999999999995 | 1330.56
Sampled | 5346 | 5497 | 1236 | 9115 | 2579 | 976.9 | 8510 | 4974 | 865 | 3364 | 1718 | 3509 | 5879 | 921.5 | 921.5 | 14371 | 6112 | 8211 | 754.5 | 1994 | 921.5 | 865 | 595.6 | 1772 | 2999 | 2118 | 2512 | 6577 | 1289 | 1394 | 2648 | 544.4 | 1341 | 3956 | 1132 | 2648 | 5497 | 3364 | 1609 | 5197 | 10425 | 544.4 | 8211 | 4420 | 9420 | 1772 | 6886 | 8510 | 1609 | 2999 | 392.4 | 976.9

## Slide 49: Milwaukee,WI. Test Site: I 794

## Slide 50: Comparison of Measured and Modeled Water Volumes and TSS Loads for Two Highway Sites in Milwaukee
Site | Runoff Volumes, cubic feet |  |  | TSS Loads, lbs. |  | 
 | Measured | Modeled | Difference | Measured | Modeled | Difference
North Site | 19,976 | 20,401 | -2% | 121 | 85 | 30%
South Site | 7,888 | 7,825 | 1% | 52 | 53 | -1%

## Slide 51
Chart: Measured versus Modeled in the Unswept Section 2007
| 39161 | 39163 | 39164 | 39196 | 39196 | 39197 | 39209 | 39216 | 39216 | 39218 | 39218 | 39251 | 39252
Measured | 998.7217 | 593.1697 | 932.369 | 626.9181 | 849.0122 | 660.6664 | 707.5709 | 411.272 | 484.4367 | 454.1724 | 453.1324 | 244.8184 | 248.8224
Modeled | 2396.38 | 2377.53 | 1304.99 | 1201.88 | 1169.6 | 1139.01 | 1132.21 | 1109.2 | 1072.18 | 1059.27 | 1041.78 | 976.9 | 972.97 | 963.52 | 856.25 | 846.62 | 811.57 | 779.44 | 776.52 | 734.18 | 681.04 | 673.08 | 666.29 | 663.97 | 632.64 | 630.48 | 553.28 | 549.76 | 522.46 | 489.76 | 486.77 | 464.59 | 436.67 | 434.73 | 423.59 | 410.91 | 398.81 | 396.52 | 395.11 | 388.54 | 320.07 | 300.55 | 301.47 | 303.8 | 315.26 | 304.53 | 302.06 | 305.12

## Slide 52
Chart: Vacuum Assisted Cleaner Productivity Curve for High Traffic Urban
| 1141.6244895825566 | 379.51181331310346 | 287.72290962807381 | 349.0626096868196 | 342.8845104003272 | 283.75127437247147 | 208.73149732220691 | 228.58967360021813 | 223.29415992608182 | 222.41157431372577 | 211.82054696545308 | 206.96632609749477 | 205.20115487278269 | 180.9300505329912 | 177.841000889745 | 192.66727309004071 | 277.57317508597919 | 238.29811533613474 | 299.19652258870252 | 253.3020707461877 | 223.29415992608182 | 1528.6382806006864 | 424.08238673708428 | 1344.6191804244493 | 270.5586203348015 | 1637.1963109204814 | 958.04668221249733
 | 373.775 | 306.4979 | 225.9419 | 243.1523 | 224.1366 | 204.3186 | 147.7529 | 173.2275 | 164.7226 | 173.4682 | 174.5112 | 168.4535 | 164.6825 | 127.5737 | 130.9035 | 146.8331 | 194.5299 | 168.0924 | 200.1062 | 181.8929 | 154.292 | 453.4885 | 314.1604 | 568.7462 | 148.1494 | 635.0605 | 363.5049

## Slide 53
Chart: Comparing Pre and Post Sweeping Monitoring versus Modeled
| 38446 | 38453 | 38456 | 38460 | 38467 | 38476 | 38488 | 38495 | 38504 | 38509 | 38516 | 38523 | 38530 | 38539 | 38544 | 38551 | 38558 | 38565 | 38579 | 38586 | 38593 | 38602 | 38607 | 38616 | 38621 | 38628 | 38635 | 38644 | 38650 | 38656 | 38663 | 38664 | 38665 | 38670
Pre Monitoring | 1337.9196 | 1120.0814 | 824.4152 | 1037.8404 | 345.0107 | 261.5663 | 317.3296 | 311.7132 | 257.9557 | 189.7559 | 207.8088 | 202.9947 | 202.1923 | 192.5641 | 188.1512 | 186.5465 | 164.4819 | 161.6736 | 175.1521 | 220.6464 | 252.3393 | 196.1747 | 238.6993 | 216.6347 | 165.2842 | 271.9968 | 229.8734 | 230.2746 | 168.0924 | 162.0748 | 202.9947 | 142.016 | 142.4172 | 153.6501
Post Monitoring | 269.991 | 271.9968 | 199.7853 | 211.4194 | 192.9653 | 178.523 | 128.7773 | 152.4466 | 144.4231 | 153.249 | 155.2548 | 149.6384 | 146.0278 | 111.1256 | 114.7361 | 129.3179 | 169.296 | 146.429 | 172.9065 | 158.8654 | 133.9925

## Slide 54: TSS Reductions for Selected Frequencies on Expanded I-39 with and without large lawn areas
Street Cleaning Frequency | Percent TSS Reduction Using Vacuum Assisted Machine |  | 
 | No Lawn | 40% Lawn Draining to Freeway | 40% Lawn Not Draining to Freeway
1\week | 70 | 49 | 65
1\4 weeks | 61 | 42 | 55
1\8 weeks | 54 | 38 | 49

## Slide 55: Conclusions
Sediment in urban streams is a serious problem.
Rains only remove a small fraction of the total particulate load from paved surfaces, mostly the smallest particles.
Street cleaning only removes a small fraction of the street dirt loading, mostly the larger particles.
The accumulation rate is much less than expected due to residual load.
Particle size distributions at outfalls are mostly made up of small particles (larger particles that wash off accumulate in sewerage)
Particle size distributions of source area sheetflows have large particles, but many of these aren’t effectively transported to outfalls.
Most models are out of balance on source area contributions.