## Slide 1: WinSLAMM v 10 Biofiltration
Using WinSLAMM v10 to Meet Urban Stormwater Management Goals

## Slide 2: We will cover . . .
Biofilter Design Concepts and Issues
Biofilter Model Algorithms
Entering Biofilter Data into the Model
Notes: The biofiltration control option replaces the simple calculation methods used for infiltration devices with the full routing calculations associated with pond storage. The “outlet” devices include natural soil infiltration (considering the wide range of variability in infiltration rates in urban soils), evaporation, surface discharges through overflows (a stand pipe or weirs), or through a rain barrel/cistern. Biofiltration controls are usually numerous in an area and can be represented in the model individually or by specifying how many of each unit is treating the flow from an individual or combination of source areas.

## Slide 3: Modeling Notes
Control practice used to model:
  Biofilters
  Rain Gardens
  Infiltration Fields
  Infiltration Trenches

## Slide 4: Modeling Notes
Biofilter routing is performed using the Modified Puls Storage – Indication Method.
Time increments are established by the user – default = 6 minutes
Yield reductions due to runoff volume reduction through infiltration and filtering through engineered soil
Notes: Biofilters can be used as control devices in individual source areas, in land uses, and as a part of the drainage system or at the outfall. To model biofilters in a source area, describe the geometry and other characteristics of a typical biofilter. Then enter the number of biofilters you want to model in the source area. The model divides the runoff volume by the number of biofilters in the source area, creates a triangular hydrograph that it routes through that biofilter, and then multiplies the resulting losses by the number of biofilters to apply the results to the source area.

## Slide 5: Control Practice Overview
Inflow rate – Low
All runoff flows through engineered soil
Native soil restricts below ground discharge
Water level below ground rises
Notes: Biofilters can be used as control devices in individual source areas, in land uses, and as a part of the drainage system or at the outfall. To model biofilters in a source area, describe the geometry and other characteristics of a typical biofilter. Then enter the number of biofilters you want to model in the source area. The model divides the runoff volume by the number of biofilters in the source area, creates a triangular hydrograph that it routes through that biofilter, and then multiplies the resulting losses by the number of biofilters to apply the results to the source area.

## Slide 6: Control Practice Overview
Inflow rate – Moderate
All runoff flows through engineered soil
Native soil restricts below ground discharge
Water level below ground rises
Water discharges through underdrain
Notes: Biofilters can be used as control devices in individual source areas, in land uses, and as a part of the drainage system or at the outfall. To model biofilters in a source area, describe the geometry and other characteristics of a typical biofilter. Then enter the number of biofilters you want to model in the source area. The model divides the runoff volume by the number of biofilters in the source area, creates a triangular hydrograph that it routes through that biofilter, and then multiplies the resulting losses by the number of biofilters to apply the results to the source area.

## Slide 7: Control Practice Overview
Inflow rate – High
Some runoff flows through engineered soil
Native soil restricts below ground discharge
Water level above ground rises
Water level below ground rises
Water discharges through underdrain
Notes: Biofilters can be used as control devices in individual source areas, in land uses, and as a part of the drainage system or at the outfall. To model biofilters in a source area, describe the geometry and other characteristics of a typical biofilter. Then enter the number of biofilters you want to model in the source area. The model divides the runoff volume by the number of biofilters in the source area, creates a triangular hydrograph that it routes through that biofilter, and then multiplies the resulting losses by the number of biofilters to apply the results to the source area.

## Slide 8: Control Practice Overview
Inflow rate – High
Some runoff flows through engineered soil
Native soil restricts below ground discharge
Water level above ground rises
Water level below ground rises
Water discharges through underdrain
and above ground
Notes: Biofilters can be used as control devices in individual source areas, in land uses, and as a part of the drainage system or at the outfall. To model biofilters in a source area, describe the geometry and other characteristics of a typical biofilter. Then enter the number of biofilters you want to model in the source area. The model divides the runoff volume by the number of biofilters in the source area, creates a triangular hydrograph that it routes through that biofilter, and then multiplies the resulting losses by the number of biofilters to apply the results to the source area.

## Slide 9: Control Practice Overview
Inflow rate – Moderate
Some runoff flows through engineered soil
Native soil restricts below ground discharge
Water level above ground falls
Water level below ground falls
Water discharges through underdrain
Notes: Biofilters can be used as control devices in individual source areas, in land uses, and as a part of the drainage system or at the outfall. To model biofilters in a source area, describe the geometry and other characteristics of a typical biofilter. Then enter the number of biofilters you want to model in the source area. The model divides the runoff volume by the number of biofilters in the source area, creates a triangular hydrograph that it routes through that biofilter, and then multiplies the resulting losses by the number of biofilters to apply the results to the source area.

## Slide 10: Control Practice Overview
Inflow rate – Moderate
All runoff flows through engineered soil
Native soil restricts below ground discharge
Water level above ground zeros out
Water level below ground falls
Water discharges through underdrain
Notes: Biofilters can be used as control devices in individual source areas, in land uses, and as a part of the drainage system or at the outfall. To model biofilters in a source area, describe the geometry and other characteristics of a typical biofilter. Then enter the number of biofilters you want to model in the source area. The model divides the runoff volume by the number of biofilters in the source area, creates a triangular hydrograph that it routes through that biofilter, and then multiplies the resulting losses by the number of biofilters to apply the results to the source area.

## Slide 11: Control Practice Overview
Inflow rate – Zero
No runoff
Native soil restricts below ground discharge
Water level below ground falls
Water discharges through underdrain, eventually only through native soil
Notes: Biofilters can be used as control devices in individual source areas, in land uses, and as a part of the drainage system or at the outfall. To model biofilters in a source area, describe the geometry and other characteristics of a typical biofilter. Then enter the number of biofilters you want to model in the source area. The model divides the runoff volume by the number of biofilters in the source area, creates a triangular hydrograph that it routes through that biofilter, and then multiplies the resulting losses by the number of biofilters to apply the results to the source area.

## Slide 12: Stormwater Constituents that may Adversely Affect Infiltration Device Life and Performance
Sediment (suspended solids) will clog device
Major cations (K+, Mg+2, Na+, Ca+2, plus various heavy metals in high abundance, such as Al and Fe) will consume soil CEC (cation exchange capacity) in competition with stormwater pollutants.
An excess of sodium, in relation to calcium and magnesium (such as in snowmelt), can increase the soil’s SAR (sodium adsorption ratio), which decreases the soil’s infiltration rate and hydraulic conductivity.

## Slide 13
A new infiltration pond after first winter; receives snowmelt from adjacent salted parking areas (plus sediment from area construction); lost almost all of the infiltration capacity and is rapidly becoming a (poorly designed) wet pond.

## Slide 14
UA Student’s Salt Addition Tests of Biofilter Media in Columns:
Lost Infiltration Rates with Clay (above 5%) and with Organic Supplements (peat in this example)

## Slide 15: Ground Water Mounding “Rules of Thumb”
Mounding reduces infiltration rate to saturated permeability of soil, often 2 to 3 orders of magnitude lower than infiltration rate.
Long narrow system (i.e. trenches) don't mound as much as broad, square/round systems

## Slide 16: Five Components to Modeling Biofilters
Structure Geometry
Outlet Information
Infiltration Data
Hydrograph and Flow Routing Information
Particle Size Distribution

## Slide 17: Biofilter Geometry
Biofilter Datum is always zero ft.

## Slide 18: Biofilter Data Entry Form
Biofilter Geometry
Outflow Structure Information

## Slide 19: Biofilter Data Entry Form
ET Plant Types Information

## Slide 20: Biofilter Data Entry Form
Engineered soil/media selection determines mixture characteristics

## Slide 21: Biofilter Data Entry Form

## Slide 22: Additional Output
Other Output Options
Time step detail
Irreducible concentration
Particulate reduction
Stage outflow
Stochastic seepage rates
Biofilter Water Balance
Stochastic seepage rates
Evapotranspiration
Notes: Biofilter stage-outflow output - Lists the discharge at each stage elevation for each biofilter outflow device.
Detailed Biofilter output - Hydraulic and stage data for each time increment in the model run.
Biofilter stochastic seepage rates - Lists the seepage rate for each event if the random infiltration rate generator option is selected.
Biofilter water balance data - Provides inflow, outflow, and volume and solids reduction fraction values for each event.
Particulate Reduction Output File - Lists the calculations that determine the particulate solids concentration for each particle size, in each rainfall event.
Irreducible Concentration Detailed Output - lists the irreducible particulate solids concentration for each particle size in each rainfall event.
Evapotranspiration Detail - Lists the evapotranspiration (ET) calculations for each time step of the model run, if ET has been selected as an output option and if there is engineered soil in the biofilter.