## Slide 1: WinSLAMM v 10 Theory and Practice
Using WinSLAMM v10 to Meet Urban Stormwater Management Goals

## Slide 2: We will cover . . .
WinSLAMM Purpose, History and Unique Features
Model Applications
Small Storm Hydrology
Basic Program Structure and Operation
Treatment Practices
Model Input/Output
Notes: 2

## Slide 3: WinSLAMM Can Answer These Types of Policy Questions . . .
What are the base level pollutant loadings for different land uses with no controls?
What flow and pollutant levels result from different development scenarios?
What are the critical sources of flows and pollutants?
How effective and cost effective are treatment practices in controlling pollutants and reducing flows?
What combinations of stormwater controls will best meet regulatory requirements?

## Slide 4: Background & History
  Development Began in mid-1970’s
    Early EPA street cleaning projects
    San Jose and Coyote Creek (CA)
    Castro Valley and other NURP projects
  Mid-1980’s - Model used in Agency Programs:
    Ottawa bacteria stormwater management program
    Toronto Area Watershed Management Strategy
    Wis. Dept. of Natural Resources: Priority Watershed Program
  Intensive data collection started in WI in early 1990s.
  First Windows version developed in 1995.
  Current graphical interface released, after three years of work, in 2012.
  Continuously being updated based on user needs and new research results.
Notes: 4
Module 4 – WinSLAMM Theory and Practice
John Voorhees, PE, PH
4

## Slide 5: Unique Features of WinSLAMM (and why it was developed!)
WinSLAMM based on actual monitoring results at many scales and conditions.
Early research project results in the 1970s did not conform to typical stormwater assumptions about rainfall-runoff relationships and sources of pollutants.
Initial versions of the model therefore focused on site hydrology and particulate sources and transport, and on public works practices.
Other control practices added as data becomes available.

## Slide 6
Controlled tests in small areas were used in conjunction with long-term rainfall/runoff monitoring at larger parking lot areas to develop actual hydrological relationships for paved areas, the most significant source of runoff for most urban areas during small to intermediate-sized rains.
This is an example of a rainfall-runoff plot from one of many controlled street washoff and runoff tests. About 1/3 of the rainfall is infiltrated through the street pavement for many of these events (up to 20 mm rains in this plot). No further infiltration was observed for larger events, resulting in classical pavement Rv values of 0.8 to 0.95 for large rains of interest for drainage design.
Pitt 1987

## Slide 7
Measured Particle Sizes, Including Bed Load Component,
at influent to the Monroe St. Detention Pond, Madison, WI
Very few of the large particles that enter the drainage systems are transported to the outfalls in typical urban drainage systems. Most (about 85% in this typical example) of the outfall particulates discharged are less than 100 µm in size.

## Slide 8
Mass balance measurements in the drainage system and at the outfall used to determine the fate and transport of the urban particulates. Much of the larger particulates that are not washed off are lost from the paved surfaces by fugitive dust by winds and traffic turbulence.
Keyes, good asphalt | 0.33 grams/vehicle-mi
Keyes, oil and screens asphalt | 18 grams/vehicle-mi
Tropicana, good asphalt | 2.5 grams/vehicle-mi
Measured fugitive dust losses from traffic (San Jose, Pitt 1979)

## Slide 9: We will cover . . .
WinSLAMM Purpose, History and Unique Features
Model Applications
Small Storm Hydrology
Basic Program Structure and Operation
Treatment Practices
Model Input/Output
Notes: 9

## Slide 10: Model Applications
Model Can Be Applied on Multiple Levels –
  Large Scale, City-wide Analysis
  Site Development Analysis (Apartment Complex, Shopping Center, Hospital Complex, Residential Development)
  Analysis of Single Practice
Notes: 10

## Slide 11: Model Applications
Large Scale, City-wide Analysis
Analysis Procedure -
  Inventory drainage basins and land uses
  Evaluate existing pollutant loads and runoff volumes (base condition).
  Adjust base condition with existing stormwater control practices.
  Evaluate additional practices to cost-effectively achieve pollutant reduction goals.
Notes: 11
Module 4 – WinSLAMM Theory and Practice
John Voorhees, PE, PH
11

## Slide 12
Model Applications
Large Scale, Regional Analysis
Pollution Load without Stormwater Control Measures
More Red – More Pollution
More Green – Less Pollution
Notes: 12
Module 4 – WinSLAMM Theory and Practice
John Voorhees, PE, PH
12

## Slide 13
Model Applications
Large Scale, Regional Analysis
Implemented Stormwater Control Measures
Green – Grass Swales
Blue – Wet Detention Ponds
Orange – Catchbasins with Sumps
Pink – Multiple Measures
Notes: 13
Module 4 – WinSLAMM Theory and Practice
John Voorhees, PE, PH
13

## Slide 14
Model Applications
Large Scale, Regional Analysis
Pollution Load with Implemented Stormwater Control Measures
Many areas went from “red” to “green”
Can concentrate on areas that are still “red”
Notes: 14
Module 4 – WinSLAMM Theory and Practice
John Voorhees, PE, PH
14

## Slide 15: Model Applications
Site Development Analysis
Analysis Procedure -
  Inventory site characteristics (soil type, percent imperviousness, etc.)
  Locate selected stormwater controls throughout the site
  Determine volume and pollutant reduction achieved with selected stormwater control practices.
Notes: 15
Module 4 – WinSLAMM Theory and Practice
John Voorhees, PE, PH
15

## Slide 16: Model Applications
Site Development Analysis
Enter all the practices for a site and link them to determine the overall runoff and pollutant reductions
Porous Pavement
Grass Swales
Wet Ponds
Biofilters
Notes: 16
Module 4 – WinSLAMM Theory and Practice
John Voorhees, PE, PH
16

## Slide 17
Model Applications
Cost Analysis
Notes: 17

## Slide 18: Capital Cost of Pond Achieving Different TSS Reductions at 100 Acre Mix of 40% Shopping Center and 60% Medium Residential
Cost-performance curves are usually not linear, with increasing unit costs as the overall treatment objective increases. For some situations, it may therefore be more cost-effective to apply moderate levels of multiple controls.
WinSLAMM can also calculate life-cycle costs that include land costs, capital costs, and operational and maintenance costs, all adjusted for financing costs and inflation factors, and expected life of project.

## Slide 19: We will cover . . .
WinSLAMM Purpose, History and Unique Features
Model Applications
Small Storm Hydrology
Basic Program Structure and Operation
Treatment Practices
Model Input/Output
Notes: 19

## Slide 20: Knowing the Runoff Volume is the Key to Estimating Pollutant Mass
There is usually a simple relationship between rain depth and runoff depth in urban systems.
Changes in rain depth affects the relative contributions of runoff and pollutant mass discharges:
  Directly connected impervious areas contribute most of the flows during relatively small rains
  Disturbed urban soils may dominate during larger rains

## Slide 21: Monitored Milwaukee Rainfall and Runoff Distributions
Small
Medium
Large
Notes: 21

## Slide 22: Monitored Milwaukee Pollutant Distribution
Small
Medium
Large
Percent Associated with Rain, or less
Rain (inches)
Notes: 22

## Slide 23: Rainfall Sorts into Three Distinct Categories
Small Rains – Accounts for most events, by number
  Typically can be easily captured for infiltration or on-site beneficial uses
  Relatively low pollutant loadings, but frequent discharges
  Key rains associated with water quality violations, e.g. bacteria and total recoverable heavy metals
  “Every” time it rains, some numeric discharge concentration objectives may be exceeded. Therefore, try to eliminate the small events

## Slide 24: Rainfall Sorts into Three Distinct Categories
Medium Rains – Responsible for most pollutant mass discharges
  Smaller events in this category can be easily captured and infiltrated or re-used
  Larger events in this category need to be treated.
  Typically responsible for about 75% of pollutant discharges

## Slide 25: Rainfall Sorts into Three Distinct Categories
Large Rains – Infrequent Large Events
  Not cost effective to treat all runoff
  Typically cause flooding and significant erosion
  Treatment practices designed for smaller storms will mitigate impacts of larger events to some extent

## Slide 26: We will cover . . .
WinSLAMM Purpose, History and Unique Features
Model Applications
Small Storm Hydrology
Basic Program Structure and Operation
Treatment Practices
Model Input/Output
Notes: 26

## Slide 27: Basic Program Structure
WinSLAMM Calculation Process
Calculate Runoff Volumes and Particulate Loadings for each Source Area
Apply Appropriate Source Area Treatment Practices
Sum Resulting Source Area Outputs
Route Totals to the Drainage System
Apply Appropriate Drainage System Treatment Practices
Route Totals to the Outfall for Volume and Pollutant Discharge to Receiving Waters
Notes: 27

## Slide 28
Outfall
Residential Land Use
Source Areas
Pitched Roofs
Driveways
Sidewalks
Small Landscaped Areas
Streets
Medium Density Residential Land Use
Residential Land Use
Source Areas
Pitched Roofs
Driveways
Small Landscaped Areas
Streets
Low Density Residential Land Use
Commercial Land Use
Source Areas
Flat Roofs
Parking
Driveways
Sidewalks
Small Landscaped Areas
Streets
Strip Commercial Land Use
Other Urban Land Use
Source Areas
Playground
Sidewalks
Large Landscaped Areas
Streets
Park Land Use
Storm Sewer Drainage System
Grass Swale Drainage System
Freeway Land Use
Source Areas
Paved Lane and Shoulders
Large Turf Areas
ROW
ROW
Notes: 28

## Slide 29
Modeled Drainage System from Previous Slide

## Slide 30
The Basic Program Structure Information is Entered in the Land Development Characteristic (.mdb) database file:
Appropriate Parameter Files
Land Use type and area
Size of all Source Areas
Source Area parameters and characteristics (soil type, connected imperviousness, street texture, etc.)
Control Practice designs
Notes: Module 4 – WinSLAMM Theory and Practice
John Voorhees, PE, PH
30

## Slide 31: Rainfall Parameter File – Can Include Many Years/Decades of Rainfall Information
Notes: 31

## Slide 32
Connected pitched roofs
Rough textured streets
Clay soils
Sandy soils
Not much difference between the different source areas for the large, drainage design storms, but much larger differences for the small and intermediate-sized rains.

## Slide 33: Particulate Solids Concentration File
Depicts the particulate solids concentrations for source areas and land uses based upon rainfall depth.
Default files available, or may be user-defined.
File extension: *.pscx
Notes: 33

## Slide 34: Sawtooth Pattern Associated with Deposition and Removal of Particulates on Urban Street
Pitt 1979
Street Dirt Washoff and Accumulation
Street Dirt Accumulation
Street Dirt Washoff or Cleaning

## Slide 35: Pollutant File
Depicts the pollutant concentrations (and variability) for source areas and land uses.
Regionally calibrated files available, or may be user-defined based on local data.
File extension: *.ppdx
Notes: Data from a pollutant value file determine, when multiplied by either a source area runoff volume or source area particulate loading, the pollutant loading from a source area. This editor creates, views, and edits pollutant probability distribution files (files with the extension .ppd) that describe pollutant concentrations or loadings that are from source areas and land uses used in WinSLAMM. This data is generally based upon pollutant loading and concentration source area and land use data collected from the study area or region. For example, particulate COD source data, in units of milligrams of COD per kilogram of suspended solids loading in the runoff, must be entered for each source area and land use of concern.
WinSLAMM calculates pollutant loadings for nine particulate and ten filterable pollutants. They are shown on the form above. The particulate pollutant units, except for Particulate Solids, are mg/kg. The filterable pollutant units are mg/l except for the metals, which are micrograms/L and the Fecal Coliform Bacterial, whose units are #/100 ml. The particulate solids (suspended solids) data is obtained in the Particulate Solids Concentration editor. The fecal coliform are retained on 0.45 micrometer filters, but generally behave like filterable pollutants in most urban runoff control practices.
The user may define up to six other pollutants in both particulate and filterable forms. Select the pollutants you want to evaluate during a model run from the Pollutant Selection form in WinSLAMM.
To use the pollutant editor, from the main menu select Utilities/Parameter Files/Pollutant Files. To view or select the an existing file, press the 'Select File' button and browse to the desired .ppd file. All pollutants with data are italicized. Select a button of an italicized pollutant to view the values. Use the scroll bar to view all the source areas. The land use values are listed at the top of the grid. To enter or change a value, place the cursor in the desired cell and change the value. The buttons at the bottom of the form allow you to print the .ppd file as an ASCII text file with the extension .txt. You can also save the file, rename the file, cancel your edits, or continue. Once you have completed your edits, save the file and then print and review it to make certain that the values are as you expected.
To enter pollutants that are not on the form, select either a Particulate or Filterable 'Other' value. Type the name of the pollutant, select the correct units, and enter the values.

## Slide 36: Critical Particle Size Files
A number of .cpz files are included with the program, or can be created using locally available psd data
For devices using sedimentation such as wet detention ponds, catchbasins, hydrodynamic devices, biofilters, grass swales, grass filters, media filters, etc.
Basic Program Operation
For 80% reduction, the particle size for control is 3 um
3 um
80%

## Slide 37: We will cover . . .
WinSLAMM Purpose, History and Unique Features
Model Applications
Small Storm Hydrology
Basic Program Structure and Operation
Treatment Practices
Model Input/Output
Notes: 37

## Slide 38: Model Output
Output Summary
Receiving Water Impacts
Land Uses and Source Area Detail
Control Device Detail
Analyzed as a single file or in batch mode
Many output options
  Control Device Detailed Output
  Hydrograph and Particle Size Distribution at each Control Practice, Land Use and Junction
Model Input/Output
Notes: 38

## Slide 39
Drainage System and Outfall Results:
Output Summary

## Slide 40
Receiving Water Impacts
Model Input/Output
Notes: Module 4 – WinSLAMM Theory and Practice
John Voorhees, PE, PH
40

## Slide 41
Detailed Output Information
Model Input/Output
Notes: 41

## Slide 42: Control Practice Summary Table
Notes: 42

## Slide 43: Similar Output for -
Particulate Solids Concentration
Particulate Solids Yield
Pollutant Concentration
Pollutant Yield
Model Input/Output
Notes: 43

## Slide 44
The WinSLAMM batch editor can be used to automatically run a large number of files, usually for integration into a GIS-based map.

## Slide 45
Commercial Areas Flow Contributions
Rains: 1: 0.01”; 2: 0.05”; 3: 0.1”; 4: 0.25”; 5: 0.5”; 6: 0.75”; 7: 1”; 8: 1.5”; 9: 2”; 10: 2.5”; 11: 3”; 12: 4”
Lincoln, NE, WinSLAMM project to identify sources and controls for bacteria (runoff volume was the critical tool)

## Slide 46
Control Program for Commercial Strip Mall Land Use | Volume Reduction (% reduction compared to base conditions for clay loam conditions in the biofilters) | Total Annual Costs ($/100 acres/yr)
Porous pavement (in half of the parking areas) | 25% | $180,400
Curb-cut biofilters (along 80% of the curbs) | 29 | $166,500
Biofilters in parking areas (10 percent of the source area) | 29 | $314,000
Small wet pond plus biofilters in parking areas (10 percent of the source area) | 29 | $341,800
Biofilters in parking areas (25 percent of the source area) | 40 | $785,000
Small wet pond plus biofilters in parking areas (10 percent of the source area) and curb-cut biofilters (along 40% of the curbs) | 43 | $424,600