## Slide 1: WinSLAMM v 10 Grass Swales and Filter Strips
Using WinSLAMM v10 to Meet Urban Stormwater Management Goals

## Slide 2: We will cover . . .
References
Processes
Entering Grass Swale Data into the Model

## Slide 3: References
EPA Report - Infiltration Through Disturbed Urban Soils and Compost (Pitt, 1999)
Alabama Highway Drainage Conservation Design Practices (Nara and Pitt, 2005)
HEC-15, Design of Roadside Channels with Flexible Linings, 2005
Results of Tests on Vegetated Waterways (Cox and Palmer, 1948
Notes: Pitt, R., Lantrip, J., Harrison, R., Henry, C., Xue, D., US EPA Research Report EPA/600/R-00/016 , Infiltration Through Disturbed Urban Soils and Compost-Amended Soil Effects on Runoff Quality and Quantity, December 1999.
Nara, Y., Pitt, R., Alabama Highway Drainage Conservation Design Practices - Particulate Transport in Grass Swales and Grass Filters, University Transportation Center for Alabama, The University of Alabama, Tuscaloosa, Alabama, Project Number 04117, November, 2006.
Cox, M., Palmer, V., Results of Tests on Vegetated Waterways, and Method of Field Application, Oklahoma Agricultural Experiment Station Miscellaneous Publication No. MP-12, January 1948.
Ebihara, T., Young, C. B., Tiware, V., Agee, L., Treatment of contaminated roadway runoff using
vegetated filter strips, Kansas Department of Transportation, Report No. K-TRAN: KU-03-5, January 2009.

## Slide 4
Head (0ft)
Date: 10/11/2004
2 ft
25 ft
6 ft
3 ft
116 ft
75 ft
TSS: 10 mg/L
TSS: 20 mg/L
TSS: 30 mg/L
TSS: 35 mg/L
TSS: 63 mg/L
TSS: 84 mg/L
TSS: 102 mg/L
University of Alabama swale test site at Tuscaloosa City Hall

## Slide 5
Runoff from
Pervious/
impervious
area
Trapping sediments
and associated pollutants
Reducing runoff
velocity
Infiltration
Reduced volume and treated
runoff
Sediment
particles
Pollutant Control in Grass Swales and Filter Strips

## Slide 6
Dynamic Wetted Width Calculation
Convert volume to flow with:
  Runoff duration = 1.2 times rainfall duration
  Complex triangular hydrograph peak to average ratio = 3.8
Width
Side slope
Slope
Manning’s n from Retardance Factor
Flow rate calculated for each time interval set by user
Calculate the wetted width from the flow rate and swale geometry using Manning’s open channel flow equation for each time step
Calculate event volume
Notes: The grass swale control device allows the user to determine the pollutant reduction and runoff volume reduction due to grass swales. The model determines the runoff volume reduction by calculating the infiltration loss for each time step. The particulate reduction is based upon the settling frequency of the particles entering the swales and the height of the grass relative to the flow depth. The grass swale filters the runoff using the settling frequency and the length of the swale. The algorithms used to determine both the Mannings n and the particle settling frequency were developed from "Alabama Highway Drainage Conservation Design Practices - Particulate Transport in Grass Swales and Grass Filters", by Yukio Nara and Robert Pitt, University Transportation Center for Alabama, University of Alabama, Tuscaloosa, Alabama, November, 2005.
Grass swale perfomance is determed by routing a complex triangular hydrograph through the swales described in the model. Runoff volume and particulate losses through particle trapping are determined differently. Runoff volume is reduced by the dynamic infiltration rate of the swales for each six minute time step of the hydrograph, and using that flow and the swale geometry and retardance to iteratively determine the depth of flow in the swale for each time step. From the depth of flow, we calculate the wetted perimeter, which, when multiplied by the total swale length, is the area used to infitrate the runoff during the time step. The detailed output for these calculations is available by selecting the 'Hydraulics Detailed Output File' checkbox from the Detailed Output Options listing. The event by event summary detailed output is available by selecting the 'Hydraulics and Concentration by Event' checkbox from the Detailed Output Options listing.

## Slide 7
Particulate Removal Calculations
Determine flow depth to grass height, for particulate reduction for each particle size increment using Nara & Pitt reference
Check particle size group limits
  Not exceed irreducible concentration value
  No filtering for particles less than 50 microns
Calculate flow velocity, settling velocity and flow depth
For each time step -
Scour adjustment by
  Flow velocity
  Impervious area
Notes: Particulate filtering is calculated for each time step using the average swale length to the outlet and the calculated depth of flow for the time step. The depth of flow and swale geometry are used to calculate the flow velocity, which in turn is used to determine the travel time and settling velocity and settling frequency for the average swale length. This information is used to determine the flow depth to grass height ratio for particulate trapping that is adapted from the Nara and Pitt reference listed above. The settling frequency and particulate reduction is calculated for each particle size fraction in the selected particle size distribution file. The detailed output for these calculations is available by selecting the 'Particulate Reduction Output File' checkbox from the Detailed Output Options listing. Each particulate reduction is then combined into one of either groups of particle sizes, where it is evaluated to determine if it is below the irreducible concentration value range for the particle size group and whether it is below 50 microns. No concentration value is allowed to go below the irreducible concentration value unless the inflow value is below that level, and no particles below 50 microns are allowed to settle out. The detailed output for these calculations is available by selecting the 'Incremental Performance Output File' checkbox and the 'Irreducible Concentration Detailed Output' checkbox from the Detailed Output Options listing.

## Slide 8: Modeling Grass Swales

## Slide 9: Five Components to Modeling Grass Swales
Swale Density
Swale Infiltration Rate
Swale Geometry
Grass Characteristics
Runoff Particle Size Distribution

## Slide 10
Swale Density
Drainage Areas
Notes: The swale length is calculated from the swale density times the area served by swales. Typical swale density values for different land uses are as follows (Pitt and McLean 1986):
Land Use Swale Density (ft/acre) .
Low density residential 160
Medium density residential 350
High density residential 375
Strip commercial 630
Shopping centers 280
Industrial 125
Not all of these land uses, especially high density residential or strip commercial areas, may be suitable for grass swales.

## Slide 11
Swale Density
Swale Density
Notes: The swale length is calculated from the swale density times the area served by swales. Typical swale density values for different land uses are as follows (Pitt and McLean 1986):
Land Use Swale Density (ft/acre) .
Low density residential 160
Medium density residential 350
High density residential 375
Strip commercial 630
Shopping centers 280
Industrial 125
Not all of these land uses, especially high density residential or strip commercial areas, may be suitable for grass swales.

## Slide 12
Swale Geometry
Swale Geometry
Notes: Grass swale data can only be entered for active land uses. To use this control practice, enter the information described below for each active land use that you want to apply grass swales to.
Area Served by Swales (ac). Enter the area of each land use that is drained by grass swales
Swale density (ft/acre). Either enter the swale density based upon site data for your model run or select a standard value based upon the appropriate land use by selecting the desired value from the array of values in the "Select Swale Density by Land Use" box. If you select a standard value, verify that the values are reasonable for your application.
Total Swale Length (ft). The program will calculate the total swale length based upon the area served by swales and the swale density. You may also directly enter the total swale length of your site.
Average Swale Length to Outlet (ft). The program will calculate the average swale length for the area served by swales in the land use, or you can enter your own value. The calculated average swale length equals 1.5 times the square root of the area served by swales. This value is used to help determine the particulate filtering capability of the swale drainage system.
Typical swale bottom width (ft). Enter the typical swale side slope for the drainage system. This must be greater than zero.
Typical swale side slope. Enter the typical swale side slope for the drainage system, in terms of 1 ft vertical to M feet horizontal, where M is the side slope.
Typical swale longitudinal slope (ft/ft). Enter the typical slope along the flow path of the swale.

## Slide 13
Average Swale Length
= AVG(∑(Segment Length/2))

## Slide 14
…or
Use the Default: 1.5 x SqRoot of the Drainage Area
Average Swale Length
= AVG(∑(Segment Length/2))

## Slide 15
Swale Dynamic Infiltration Rate
Values listed in WinSLAMM are about ½ of the static infiltration rate for a given soil
Infiltration Rate
Notes: Grass swale data can only be entered for active land uses. To use this control practice, enter the information described below for each active land use that you want to apply grass swales to.
Swale Dynamic Infiltration Rate (in/hr). Enter the dynamic swale infiltration rate. This value is typically about one-half of the infiltration rate as measured using a double-ring infiltrometer. Either enter the infiltration rate based upon site data for your model run or select a standard value based upon the appropriate soil type from the 'Select infiltration rate by soil type' data box, and then selecting the desired value. If you select a standard value, verify that the values are reasonable for your application.

## Slide 16
Swale Retardance Factor
Swale Retardance Factor
Retardance Classification system is from HEC-15, Classification of Vegetal Covers
Mannings n =
f(velocity, hydraulic radius, retardance)
Notes: Grass swale data can only be entered for active land uses. To use this control practice, enter the information described below for each active land use that you want to apply grass swales to.
Swale Retardance Factor. Select the swale retardance factor (either A, B, C, D or E) from the drop-down menu. The retardance factor describes the type and height of the grass, which is used to determine the Manning's n value using the equations provided in HEC-15 (April, 1988).

## Slide 17
Enter Grass Height and Particle Size Distribution to Determine Particle Size Filtering
Particle Size File
Particle Size Distribution File not accessible if Flows and Particle Sizes transferred through the drainage system
Notes: Grass swale data can only be entered for active land uses. To use this control practice, enter the information described below for each active land use that you want to apply grass swales to.
Typical Grass Height (in). Enter the typical height of the grass found in the swale. This value is used to help determine the particulate removal rate of the swale.
Particle Size Distribution File. Click on the cell to the right of each active land use, and then press the 'Select Critical Particle Size File' button to enter the particle size distribution file you want to use to evaluate the swale performance. If you want to apply the file name in the residential land use to all the land uses, press the button below the Particle Size Distribution File Data Grid.

## Slide 18
Infiltration Rate Adjustment
Static Infiltration Rate
Dynamic Infiltration Rate
This is what you start with
Notes: The model adjusts the infiltration rate based upon the slope of the grass swale. If the slope is greater than two percent, then the model uses the dynamic infiltration rate entered by the user. If the slope is less than one-half percent, then the model assumes that the infiltration rate is twice the dynamic rate (the static infiltration rate) to account for the microstorage typically found in nearly flat grass drainage systems because of the difficulty grading these flatter channels. If the slope is between one-half and two percent, the model calculates the infiltration rate based upon a linear slope calculation.

## Slide 19
Additional Output
Detailed Hydraulics By Time Step
Hydraulics And Concentration By Event
Incremental Performance
Irreducible Concentration
Particulate Reduction by Particle Size
Iterative calculation to determine swale height and wetted perimeter for each runoff event
SwaleQ = 1.486 / n * (h * BottomWidth + SideSlope * h ^ 2) ^ (5 / 3) / (BottomWidth + h * Sqr(SideSlope * SideSlope + 1) * 2) ^ (2 / 3) * Sqr(LongSlope)
Notes: GrassSwaleHydraulics.csv – This file documents the iterative calculation made to determine the flow depth and wetted perimeter, based upon the entered swale geometry, for each rainfall event in a model run. Qin is flow rate based upon the runoff volume, runoff duration, and peak-to-average flow rate for the event, Qcalc is the flow calculated from the or depth of water in the swale (h). Once the difference between the two flow values is less than 0.001 cfs, the iteration process is complete for that time step.
Particulate Reduction Output File – This file provides detailed output of how grass swales perform for each time step, for each particle size distribution fraction.
Incremental Performance Output File – This file lists the flow rate, volume and particulate removal performance of a swale for each time step.
Hydraulics and Concentration by Event – This file describes the performance of the swale from a water balance perspective for each event in the model run. It also includes concentration and loading information for each event.
Irreducible Concentration Detailed Output – This file lists the irreducible concentration determinations for each time step, for each group of particle sizes (eight in total) for the model run.

## Slide 20: Modeling Filter Strips

## Slide 21
Runoff from
Pervious/
impervious
area
Reduced volume and treated
runoff
Runoff Volume Reduction in
Filter Strips
Runoff Volume Reduced in Each Time Step as Water Flows Over Filter

## Slide 22
Grass Filter Strips
Assumptions:
Flow over surface modeled as sheet flow
All particle sizes are treated
Effective treatment length reduced based upon slope
  <0.02 ft/ft – 3 ft reduction
  >0.05 ft/ft – 10 ft reduction
  else – 6 ft reduction
Irreducible concentration a function of particle size

## Slide 23: Five Components to Modeling Filter Strips
Infiltration Rate
Geometry
Grass Characteristics
Clogging and Runoff Particle Size Distribution

## Slide 24
Geometry
Geometry
Note direction of flow length and filter strip width
The filter strip area to drainage area ratio must be greater than 0.05
Notes: Grass swale data can only be entered for active land uses. To use this control practice, enter the information described below for each active land use that you want to apply grass swales to.
Area Served by Swales (ac). Enter the area of each land use that is drained by grass swales
Swale density (ft/acre). Either enter the swale density based upon site data for your model run or select a standard value based upon the appropriate land use by selecting the desired value from the array of values in the "Select Swale Density by Land Use" box. If you select a standard value, verify that the values are reasonable for your application.
Total Swale Length (ft). The program will calculate the total swale length based upon the area served by swales and the swale density. You may also directly enter the total swale length of your site.
Average Swale Length to Outlet (ft). The program will calculate the average swale length for the area served by swales in the land use, or you can enter your own value. The calculated average swale length equals 1.5 times the square root of the area served by swales. This value is used to help determine the particulate filtering capability of the swale drainage system.
Typical swale bottom width (ft). Enter the typical swale side slope for the drainage system. This must be greater than zero.
Typical swale side slope. Enter the typical swale side slope for the drainage system, in terms of 1 ft vertical to M feet horizontal, where M is the side slope.
Typical swale longitudinal slope (ft/ft). Enter the typical slope along the flow path of the swale.

## Slide 25
Infiltration Rate
Infiltration Rate
Listed native soil infiltration rates based upon field double ring infiltrometer measurements
Depth of Water in Filter Strip | Infiltration Rate (in/hr)
<= 0.015 | Entered Rate x 2 (Static Infiltration Rate)
> 0.015 and < 0.03 | Interpolated Between the Two Rates
>= 0.03 | Entered Rate (Dynamic Infiltration Rate)
Notes: Grass swale data can only be entered for active land uses. To use this control practice, enter the information described below for each active land use that you want to apply grass swales to.
Area Served by Swales (ac). Enter the area of each land use that is drained by grass swales
Swale density (ft/acre). Either enter the swale density based upon site data for your model run or select a standard value based upon the appropriate land use by selecting the desired value from the array of values in the "Select Swale Density by Land Use" box. If you select a standard value, verify that the values are reasonable for your application.
Total Swale Length (ft). The program will calculate the total swale length based upon the area served by swales and the swale density. You may also directly enter the total swale length of your site.
Average Swale Length to Outlet (ft). The program will calculate the average swale length for the area served by swales in the land use, or you can enter your own value. The calculated average swale length equals 1.5 times the square root of the area served by swales. This value is used to help determine the particulate filtering capability of the swale drainage system.
Typical swale bottom width (ft). Enter the typical swale side slope for the drainage system. This must be greater than zero.
Typical swale side slope. Enter the typical swale side slope for the drainage system, in terms of 1 ft vertical to M feet horizontal, where M is the side slope.
Typical swale longitudinal slope (ft/ft). Enter the typical slope along the flow path of the swale.

## Slide 26
Retardance
Retardance Classification system is from HEC-15, Classification of Vegetal Covers
Mannings n =
f(velocity, hydraulic radius, retardance)
Notes: Grass swale data can only be entered for active land uses. To use this control practice, enter the information described below for each active land use that you want to apply grass swales to.
Area Served by Swales (ac). Enter the area of each land use that is drained by grass swales
Swale density (ft/acre). Either enter the swale density based upon site data for your model run or select a standard value based upon the appropriate land use by selecting the desired value from the array of values in the "Select Swale Density by Land Use" box. If you select a standard value, verify that the values are reasonable for your application.
Total Swale Length (ft). The program will calculate the total swale length based upon the area served by swales and the swale density. You may also directly enter the total swale length of your site.
Average Swale Length to Outlet (ft). The program will calculate the average swale length for the area served by swales in the land use, or you can enter your own value. The calculated average swale length equals 1.5 times the square root of the area served by swales. This value is used to help determine the particulate filtering capability of the swale drainage system.
Typical swale bottom width (ft). Enter the typical swale side slope for the drainage system. This must be greater than zero.
Typical swale side slope. Enter the typical swale side slope for the drainage system, in terms of 1 ft vertical to M feet horizontal, where M is the side slope.
Typical swale longitudinal slope (ft/ft). Enter the typical slope along the flow path of the swale.

## Slide 27
Surface clogging due to source area loading, accumulates over time.
Infiltration rate clog adjustment = Trapped Mass/Clogging Load
If the swale does not clog after 10 years, assume:
It will not clog
Maintain the 10 year adjusted infiltration rate
Surface Clogging
Surface Clogging

## Slide 28
Additional Output
Hydraulic Details by Time Step
Incremental PSD and Concentration
Particulate Reduction by Particle Size
Irreducible Concentration
Hydraulics and Concentration By Event
Rain No. | Rainfall Depth (in) | Filter Strip No. | SA/LU Runoff Volume (cf) | Runoff Volume to FS (cf) | Runoff Volume Bypassing FS (cf) | Runoff Volume Infiltrated (cf) | FS Effluent Volume (cf) | Total Effluent Volume (cf) | Influent Conc (mg/l) | Infil. Rate Clogging Adj. Factor (Fraction) | Adj. Infil. Rate (in/hr) | TSS Eff Conc Reduct. Ratio | Effluent Conc Before Ratio Adj. | Final Effluent Conc (mg/l) | Influent Load (lbs) | Effluent Load (lbs) | Cum. Clogging Load (lbs/sf) | Maximum Velocity (ft/s) | Maximum Depth (ft) | Maximum Shear (lb/sf)
40 | 0.01 | 1 | 3.22707 | 3.22707 | 0 | 3.229954 | 0 | 0 | 130 | 0.0000 | 0.0446 | 0.108969 | 15 | 0 | 0.02619 | 0.0000 | 0.0000 | 0.0050 | 0.0027 | 0.0051
41 | 0.01 | 1 | 3.22707 | 3.22707 | 0 | 3.229957 | 0 | 0 | 130 | 0.0000 | 0.0446 | 0.108969 | 15 | 0 | 0.02619 | 0.0000 | 0.0000 | 0.0051 | 0.0028 | 0.0052
42 | 0.01 | 1 | 3.22707 | 3.22707 | 0 | 3.229948 | 0 | 0 | 130 | 0.0000 | 0.0446 | 0.108969 | 15 | 0 | 0.02619 | 0.0000 | 0.0000 | 0.0051 | 0.0028 | 0.0052
43 | 0.33 | 1 | 735.6448 | 735.6448 | 0 | 169.7649 | 565.9003 | 565.9003 | 130 | 0.0002 | 0.0446 | 0.108969 | 19.28059 | 31.34552 | 5.97022 | 1.1074 | 0.0006 | 0.0235 | 0.0276 | 0.0516
44 | 0.07 | 1 | 106.7271 | 106.7271 | 0 | 86.29122 | 20.43898 | 20.43898 | 130 | 0.0002 | 0.0445 | 0.108969 | 15 | 27.53138 | 0.866157 | 0.0351 | 0.0007 | 0.0109 | 0.0087 | 0.0162
45 | 0.43 | 1 | 1013.367 | 1013.367 | 0 | 269.4128 | 743.9595 | 743.9595 | 130 | 0.0004 | 0.0445 | 0.108969 | 17.9533 | 30.16286 | 8.224113 | 1.4009 | 0.0016 | 0.0221 | 0.0252 | 0.0471
46 | 2.59 | 1 | 8609.945 | 8609.945 | 0 | 318.1631 | 8291.851 | 8291.851 | 130 | 0.0020 | 0.0445 | 0.108969 | 40.80983 | 50.52875 | 69.87511 | 26.1559 | 0.0070 | 0.0497 | 0.0847 | 0.1586
47 | 0.34 | 1 | 762.9528 | 762.9528 | 0 | 103.7634 | 659.2626 | 659.2626 | 130 | 0.0022 | 0.0445 | 0.108969 | 21.70889 | 33.50921 | 6.191841 | 1.3791 | 0.0076 | 0.0292 | 0.0383 | 0.0717
48 | 0.32 | 1 | 708.6318 | 708.6318 | 0 | 103.519 | 605.1809 | 605.1809 | 130 | 0.0023 | 0.0445 | 0.108969 | 21.58258 | 33.39666 | 5.750992 | 1.2617 | 0.0082 | 0.0284 | 0.0366 | 0.0686
49 | 0.51 | 1 | 1239.519 | 1239.519 | 0 | 239.1143 | 1000.422 | 1000.422 | 130 | 0.0026 | 0.0444 | 0.108969 | 20.72677 | 32.63411 | 10.05948 | 2.0381 | 0.0092 | 0.0253 | 0.0308 | 0.0577
50 | 0.13 | 1 | 236.219 | 236.219 | 0 | 97.26946 | 138.9721 | 138.9721 | 130 | 0.0027 | 0.0444 | 0.108969 | 15 | 27.53138 | 1.917065 | 0.2389 | 0.0094 | 0.0183 | 0.0189 | 0.0355
51 | 0.24 | 1 | 503.1494 | 503.1494 | 0 | 35.03768 | 468.561 | 468.561 | 130 | 0.0028 | 0.0444 | 0.108969 | 31.2251 | 41.98845 | 4.083373 | 1.2282 | 0.0098 | 0.0384 | 0.0576 | 0.1079
Notes: GrassSwaleHydraulics.csv – This file documents the iterative calculation made to determine the flow depth and wetted perimeter, based upon the entered swale geometry, for each rainfall event in a model run. Qin is flow rate based upon the runoff volume, runoff duration, and peak-to-average flow rate for the event, Qcalc is the flow calculated from the or depth of water in the swale (h). Once the difference between the two flow values is less than 0.001 cfs, the iteration process is complete for that time step.
Particulate Reduction Output File – This file provides detailed output of how grass swales perform for each time step, for each particle size distribution fraction.
Incremental Performance Output File – This file lists the flow rate, volume and particulate removal performance of a swale for each time step.
Hydraulics and Concentration by Event – This file describes the performance of the swale from a water balance perspective for each event in the model run. It also includes concentration and loading information for each event.
Irreducible Concentration Detailed Output – This file lists the irreducible concentration determinations for each time step, for each group of particle sizes (eight in total) for the model run.