## Slide 1: WinSLAMM v 10.1 Control Practice Cost Analysis/Batch Processor
Using WinSLAMM v10 to Meet Urban Stormwater Management Goals

## Slide 2: We will cover . . .
Cost Analysis Overview
Sources of Cost Data
Entering Cost Data
Running the model with Cost Data and Reviewing Cost Output

## Slide 3: We will cover . . .
Cost Analysis Overview
Sources of Cost Data
Entering Cost Data
Running the model with Cost Data and Reviewing Cost Output

## Slide 4: Cost Analysis Overview
Calculates the cost of the control practices listed in a model run
Allows you to compare the cost of different sets of practices
Provides the option of applying either pre-determined costs or user-defined costs
Doesn’t evaluate the cost reductions due to the use of control practices, ie, no asphalt pavement reduction determined if porous pavement is used.
What Does the Cost Analysis Program Do?
Notes: WinSLAMM will evaluate the costs of control practices using either pre-determined unit cost data or from user-defined cost data. This module works by calculating the quantity of a key component for a control practice - for example, the linear feet of grass swales in a model - and then multiplying that quantity by the unit cost of the practice. The cost components that the model evaluates are capital costs, maintenance costs and land costs. The cost data output is found on the summary tab or as one of two text files - as a cost total for all the practices in a model run and as an itemized list of costs for each practice in a model run. The model will adjust costs based upon a pre-determined City Cost Index or through a user-defined cost index value, and will calculate both the present value of all costs and the annual value of all costs, based upon the estimated life of the project.
Control practice costs are evaluated using a Control Practice Cost File. This file has the following components:
Summary Data
Detention Pond
New Device (reserved for addtional control device)
Porous Pavement
Hydrodynamic Device (currently not available)
Street Cleaning
Biofiltration Device
Catchbasin Cleaning
Upflow Filter (currently not available)
Grass Swales

## Slide 5: Cost Analysis Overview
Pipe System Opportunity Cost for Grass Swale Drainage System – cost spreadsheet v12.1b.xls
Notes: To compare the cost of a conventional storm sewer pipe drainage system with the cost of a grass swale drainage system, use WinSLAMM to determine the grass swale drainage system cost. To estimate the cost of a storm sewer drainage system, use the spreadsheet provided with the program: Spreadsheet to Estimate Conventional Drainage Costs.xls

## Slide 6: Cost Analysis Overview
How are the Cost Values Normalized?
Total Present Worth = Capital Cost +
Land Cost +
Present Worth of
Annual Maintenance Cost
P
A
A
A
A
A
A
1
2
4
3
n
((i+1)N-1) / (i*(1+i)N )
Notes: The cost components that the model evaluates are capital costs, maintenance costs and land costs. The model will calculate both the present value of all costs and the annual value of all costs, based upon the estimated life of the project. The present value, or total present worth, or present worth of a uniform series, of all costs is calculated by:
Total Present Worth = Capital Cost + Land Cost + (P/A)in (Annual Maintenance Cost)
Where (P/A)in = [(1 + I)n – 1]/[1(1 + I)n]
n = project life
i = cost of capital or interest rate

## Slide 7: Cost Analysis Overview
How are the Cost Values Normalized?
Uniform Series Worth = Annual Value of (Capital Cost + Land Cost) +
Annual Maintenance Cost
P
A
A
A
A
A
A
1
2
4
3
n
(i*(1+i)N ) / ((i+1)N-1)
Notes: The cost components that the model evaluates are capital costs, maintenance costs and land costs. The model will calculate both the present value of all costs and the annual value of all costs, based upon the estimated life of the project. The annualized value of all costs, or uniform series worth of a present sum, or capital recovery factor, of all costs is calculated by:
Annualize Value = (A/P)in [Capital Cost + Land Cost] + Annual Maintenance Cost
Where (A/P)in = [1(1 + I)n]/[(1 + I)n – 1]
n = project life
i = cost of capital or interest rate

## Slide 8: Cost Analysis Overview
Edit and Save the Cost Template.csv File
Select the Cost Data File for a Model Run
Run the Program
Review the Cost Output
What is the General Cost Evaluation Process?

## Slide 9: We will cover . . .
Cost Analysis Overview
Sources of Cost Data
Entering Cost Data
Running the model with Cost Data and Reviewing Cost Output

## Slide 10: Sources of Cost Data
Pre-Determined Costs
  SEWRPC 1991 Cost Report
  Many EPA cost summary reports
  Costs Updated Using ENR Cost Indices
  Cost Indices Available for 20 Cities

## Slide 11: Sources of Cost Data
Pre-Determined Costs for each practice
  Costs Available for –
    Wet Detention
    Porous Pavement
    Grass Swales
    Street Cleaning
    Catchbasins
    Infiltration Trenches

## Slide 12: Sources of Cost Data
User-Defined Costs for Each Practice
  Enter Items that Define the Practice
  Select Unit
  Enter Cost per Unit
  Enter Quantity
  Program Calculates Cost
Program Determines Total Unit Cost
Enter Routine Maintenance Cost

## Slide 13: We will cover . . .
Cost Analysis Overview
Sources of Cost Data
Entering Cost Data
Running the model with Cost Data and Reviewing Cost Output

## Slide 14
Edit and Save the Cost Template.csv File
On the Summary Data Page
  Enter project life and interest rate information
  Enter Land Costs
  Select Cost Index
For Each Control Practice
  Select either Pre-Determined or User-Defined Costs
  For Pre-Determined Costs, select Cost Range
  For User-Defined Costs, enter Cost Data
  Enter Land Use Multiplier
Re-name and Save Cost Data File

## Slide 15: Edit and Save the Cost Template.csv File
From the Main Menu go to the Tools/Access Cost Data Summary Tab . . .
Notes: The summary data tab contents include:
Select File: Press to open an existing cost data file. Cost data files must have the extension '.csv'
Save File: Press to save the current cost data file using the current cost data file name. You must save the cost data file in order for the program to use your changes.
Save File As . . . : Press to save the current cost data file with a different name.
File Description: Enter a description of the cost data file. The description will be saved with the file data.

## Slide 16: Edit and Save the Cost Template.csv File
Control Practice Cost Tabs and Summary Data Tab
Cost File Management
Summary Data Tab
Notes: The summary data tab contents include:
Select File: Press to open an existing cost data file. Cost data files must have the extension '.csv'
Save File: Press to save the current cost data file using the current cost data file name. You must save the cost data file in order for the program to use your changes.
Save File As . . . : Press to save the current cost data file with a different name.
File Description: Enter a description of the cost data file. The description will be saved with the file data.

## Slide 17: Edit and Save the Cost Template.csv File
Land Use Costs
Interest Rate and Project Life
Cost Index Selection
Summary Data Tab
Notes: Interest Rate on Debt Capital: Enter the interest rate that you want the program to use for net present value and annual value cost calcuations. The program will use this value and the project life to convert annual costs to a present value and to amortize present capital costs over the life of the project.
Project Life: Enter the number of years that you want to amortize the life of the project over.
Land Cost by Land Use: Enter the estimated or typical cost of land per acre for the land uses listed on the form. You can enter zero values if the cost of land is not relevant for your analysis.
Cost Index Selection: Cost indices only are applied to those practices in which you decide to use pre-determined costs. If you elect to use a City Cost Index, use the pull down menu to select the city that most accurately reflects the cost difference between your area and the national average. The program will then calculate the cost index multiplier based upon your selection. You may also edit the cost data file to add your own city and it's index. All index data are from the Engineering News Record (ENR). The baseline national cost index is the average of twenty cities whose cost indices are listed in the ENR.
Select 'User Defined Cost Index Values' if you want to enter your own index values. You may then enter either the current year cost index value for your area (select the appropriate radio button and then enter the value). The program will use the index value to calculate an index mutiiplier based upon the Baseline Cost Index Value. To change this value, you must make the appropriate modifcation to the cost data file. You can also enter a 'User Defined Cost Index Multiplier' directly by selecting the appropriate radio button and then entering a value.

## Slide 18: Edit and Save the Cost Template.csv File
Pre-Determined Cost Table
Pre-Determined Capital Cost Range
Wet Detention Pond Cost Data
Notes: Wet Detention Pre-Determined Costs
The pre-determined wet detention pond costs are calculated from the table on the wet detention pond cost data form. If you elect to use this table, then you must also select a capital cost range of Low, Medium, or High. The cost data shown in this table is adjusted for inflation using the cost index (CI) multiplier from the Summary Data page to illustrate the changes that occur to the coefficients due to the CI. The program calculates the cost of a wet detention pond by calculating the total volume of the pond and then selecting the capital cost from the table based upon the total pond volume and the capital cost range you selected. If the total pond volume of a pond is between two of the values on the table, then the program interpolates the value from the cost table. Note that the pre-determined annual O&M cost includes sediment removal. The label below the pre-determined cost table shows the city or the user-defined cost index multiplier that has been selected for the cost index.

## Slide 19: Edit and Save the Cost Template.csv File
User-Defined Cost Table
Maintenance Cost Data
- Sediment Removal Costs
- Routine Maintenance Cost
Wet Detention Pond Cost Data
Total Unit Cost
per 1000 cubic feet
Land Area Multiplier
Notes: Wet Detention User-Defined Maintenance Costs
There are two types of maintenance costs for wet detention ponds - routine maintenance costs and sediment removal costs. The routine maintenance costs are calculated by multiplying the volume of the pond by the value you enter.
The sediment removal cost is calculated by determining:
1. The amount of sediment (mass in lbs) that is deposited in the pond for however many years you enter for the sediment removal frequency.
2. The cost of removing that sediment. To convert sediment mass to sediment volume, the model assumes that the sediment specific gravity is 2 50 and that the porosity of the sediment is 0.7.
3. The present value of the sediment removal costs, assuming that at least one sediment removal will occur at the listed sediment removal frequency rate.
4. The annualized sediment removal cost based upon the life of the project.
5. The annual maintenance cost, which is the sum of the annual routine maintenance cost and the annualized sediment removal cost.
Sediment cost calculation output details are listed in the Cost Output Option Number 3, which is a list of the costs of each control device from either one file or a group of .dat files run as a set.

## Slide 20: Edit and Save the Cost Template.csv File
Total Unit Cost
Total Unit Cost
per 1000 cubic feet
Notes: Wet Detention User-Defined Maintenance Costs
There are two types of maintenance costs for wet detention ponds - routine maintenance costs and sediment removal costs. The routine maintenance costs are calculated by multiplying the volume of the pond by the value you enter.
The sediment removal cost is calculated by determining:
1. The amount of sediment (mass in lbs) that is deposited in the pond for however many years you enter for the sediment removal frequency.
2. The cost of removing that sediment. To convert sediment mass to sediment volume, the model assumes that the sediment specific gravity is 2 50 and that the porosity of the sediment is 0.7.
3. The present value of the sediment removal costs, assuming that at least one sediment removal will occur at the listed sediment removal frequency rate.
4. The annualized sediment removal cost based upon the life of the project.
5. The annual maintenance cost, which is the sum of the annual routine maintenance cost and the annualized sediment removal cost.
Sediment cost calculation output details are listed in the Cost Output Option Number 3, which is a list of the costs of each control device from either one file or a group of .dat files run as a set.

## Slide 21: Edit and Save the Cost Template.csv File
Total Unit Cost Basis for User Defined Costs
Control Practice | Total Unit Cost Units
Wet Detention Pond | Sum of user-defined costs ($) / 1000 cf Pond Volume (datum to highest elevation)
Porous Pavement | Sum of user-defined costs ($) / sf of Porous Pavement
Street Cleaning | Street Cleaner capital cost ($) / Total curb-miles swept per year
Biofiltration | Sum of user-defined costs ($) / cy Cut/Fill Volume
Catchbasin Cleaning | Sum of user-defined costs ($) / Unit
Grass Swales | Sum of user-defined costs ($) / lf of grass swale

## Slide 22: We will cover . . .
Cost Analysis Overview
Sources of Cost Data
Entering Cost Data
Running the Model with Cost Data and Reviewing Cost Output

## Slide 23: Two Types of Cost Output
File Run - Capital, Land, and Maintenance Costs on the Summary Tab of a WinSLAMM Model Run
Group File Run - Capital, Land, and Maintenance Costs included with the output when you run a set of .mdb files using the Batch Processor

## Slide 24
Enter the Cost Data File Name in the Current File Data Window
1. Output on a Model Run Summary Tab
Notes: To include cost data in the output of a .dat file:
1. Select the 'Current File Data' button.
2. Check the 'Use Cost Estimation Option' checkbox.
3. Press the 'Select Cost Data File' button and select the cost data file that you just created.
4. Press 'Continue' and run the model (assuming that you have entered all other necessary data).
5. The cost data output will appear in the Output Summary tab.

## Slide 25
Total Control Practice Costs
1. Output on a Model Run Summary Tab
Notes: Cost analysis of the controls from one .dat file model run.
You can review the costs expected from the controls you place in a .dat file by checking the 'Use Cost Estimation Option' box in the Current File Data form and selecting a cost data file. You must also have selected Output Option 1 to 4. You will get the Output Summary page, which will include a summary of the cost data for the model run. The cost summary includes:
1. The capital cost of all practices included in the .dat file.
2. The cost of land for all practices included in the .dat file.
3. The annual maintenance cost of all practices included in the .dat file.
4. The present value of all costs included in the .dat file. This is the sum of the capital cost, land cost, and the present value of the maintenance costs. The present value is determined from the interest rate on debt capital and the project life you entered on the summary data tab of the Control Practice Cost Data window.
5. The annualized value of the costs of the practices in the .dat file. This is the sum of the annualized value of the capital and land costs, and the annual maintenance costs. The annualized value is determined from the interest rate on debt capital and the project life you entered on the summary data tab of the Control Practice Cost Data window.

## Slide 26
Enter the Cost Data File Name by checking the box and pressing the ‘Select Cost Data File’ Window
2. Output from a Set of .mdb Files
Notes: Summary cost analysis of a set of .dat files run as a group.
If you use the batch file option of running a set of .dat files a group, the output of each of the files you selected will be summarized in a comma-separated-value file called "DATSetOutput.csv", which will be located in the same directory that has the .dat files you ran. If you have elected to include cost estimates, then cost summary data will also appear with the runoff and pollutant output, as is shown on the next slide.

## Slide 27
Import the output file ‘MDBSetOutput.CSV’ into Excel
2. Output from a Set of .mdb Files
Cost Output for each .mdb file
Notes: Summary cost analysis of a set of .dat files run as a group.
If you use the batch file option of running a set of .dat files as a group, the output of each of the files you selected will be summarized in a comma-separated-value file called "DATSetOutput.csv", which will be located in the same directory that has the .dat files you ran. Above is an example of this output for six .dat files run as a set. This file lists, for each .dat file you selected, the values shown in the top row of the table. It will also show pollutant yields if you selected any pollutants for analysis.
The comma-separated-value file is easily imported into Excel for formatting and further analysis, as shown above.

## Slide 28
Import the output file ‘MDBSetOutputCostDetail.CSV’ into Excel
2. Output from a Set of .mdb Files
Cost Information for each control practice
Notes: A detailed listing of each set of control device costs from either one file or a group of .dat files run as a set
If you use the batch file option of running a set of .dat files as a group, the output of each of the files you selected will also be detailed in a comma-separated-value file called "DATSetOutputCostDetail.csv", which will be located in the same directory that has the .dat files you ran. This file provides additional information about each of the control practices in each .dat file. This comma-separated-value file lists, for each .dat file you selected, the values shown in the top row of the table below for each control practice you modeled in each .dat file. In the example shown on this slide, note the following:
1) There were six files run in the set of .dat files. Each file is assigned a number, starting with zero.
2) There were two source areas in the 'Inst S Ind S.dat' file name.
3) The cost data file had no land costs, so no land costs were analyzed.
4) Two biofilters were modeled, so the biofilter calculated the biofilter volume above the rock.
5) The 'Hunts indus A site bioret' and 'Hunts indus B site bioret' have a Source Area Number of 0 because they are land use biofilters, and so have no source area.
The sediment removal mass, volume, and costs are only applicable for wet detention ponds that are analyzed with a cost data file that has user-defined costs listed for wet detention ponds, including sediment removal costs. This analysis was done using the pre-determined costs, so no sediment analysis was performed.
The comma-separated-value file is easily imported into Excel for formatting and further analysis, as shown above.

## Slide 29
Import the output file ‘MDBSetOutputCostDetail.CSV’ into Excel
2. Output from a Set of .mdb Files
Additional Detention Pond Sediment and Biofilter Volume Information
Notes: Additional detention pond sediment and biofilter volume information is only available if user-defined costs are used.

## Slide 30
Import the output file ‘MDBSetOutputCostDetail.CSV’ into Excel
2. Output from a Set of .mdb Files
Present Value and Annual Value Cost Information

## Slide 31
Chart: Cost per cubic foot Runoff Volume Reduced
| 68.319999999999993 | 24.47 | 16.940000000000001 | 86.91 | 87.2 | 27.39 | 27.16 | 86.91 | 87.2 | 23.5 | 78.59 | 79.34 | 17.12 | 78.59 | 79.34 | 17.260000000000002 | 67.66
Cost per cubic foot Runoff Volume Reduced ($/cf) | 0.03 | 0.1 | 0.02 | 0.08 | 0.07 | 0.14 | 0.1 | 0.08 | 0.07 | 0.15 | 0.07 | 0.06 | 0.06 | 0.07 | 0.06 | 0.08 | 0.04
Plot Data to Identify Sets of Cost-Effective Stormwater Control Programs
Porous pavement
Porous pavement with grass swales
Porous pavement with biofilters