## Slide 1: WinSLAMM v 10 Porous Pavement
Using WinSLAMM v10 to Meet Urban Stormwater Management Goals

## Slide 2: We will cover . . .
Entering Porous Pavement Data into the Model
Modeling Notes

## Slide 3: Porous Pavement Cross Section

## Slide 4: Porous Pavement Data Requirements
Pavement Geometry and Properties
Outlet/Discharge Options
Surface Pavement Layer and Cleaning Data

## Slide 5
Area – runoff from the Total Area drains to the Porous pavement area
Pavement Geometry and Properties
Outlet and Discharge Options

## Slide 6
Schematic with entered data
Cleaning Frequencies
Notes: The porous pavement control option now has full routing calculations associated with pond storage in conjunction with other porous pavement features. The “outlet” options for porous pavement include subgrade seepage as well as an optional underdrain, which is modeled as an orifice. The porous pavement control device option also has a surface seepage rate that limits the amount of runoff that can enter the storage system. This surface seepage rate can be reduced to account for clogging over time, and the surface seepage rate can be partially restored with cleaning at a stated cleaning frequency. The porous pavement control device infiltrates water originating from the rainfall hitting the pavement surface area only - it does not accept run-on from other surfaces. The runoff volume reaching the porous pavement surface is therefore equal to the rainfall volume directly falling on the porous pavement. The porous pavement surface area can be any material, including paver blocks, porous concrete, porous asphalt, or any other porous surface. Porous pavements are usually installed over a subsurface storage layer that can dramatically increase the infiltration performance of the device.
The porous pavement control option can be used as a control device only in individual source areas. Porous pavements are usually located at paved parking and storage areas, paved playgrounds, paved driveways, or paved walkways. You should typically use porous pavements in relatively clean areas (walkways or driveways or other surfaces that receive little traffic, for example), to minimize groundwater contamination potential. Porous pavements direct the infiltrating water to subsurface soil layers, usually beneath much or the organic surface soils that tend to sorb many pollutants. Salts used for ice control in northern areas are also problematic when considering infiltrating stormwater. Therefore, only use porous pavements in areas needing minimal salt applications. Consider biofiltration devices to infiltrate water from more contaminated sites, as they can use amended soils to help trap contaminants before infiltration, or use other appropriate pre-treatment before infiltration. No common pretreatment device is suitable for the removal of salts, however, so minimal use is the preferred control option in that case.
To model porous pavement in a suitable source area, describe the geometry and other characteristics of a typical porous pavement surface. The model computes the runoff volume, equal to the rainfall volume, and then creates a complex triangular hydrograph that is used to statistically describe a random rainfall pattern (the flow duration equals the rain duration) that it routes through that porous pavement system.
See the WinSLAMM Help file for additional information about the porous pavement control device.

## Slide 7
Run-on Allowed
Surface Clogging Option 1

## Slide 8
Surface Clogging Option 2
Surface Pavement Percent Solids Removal Upon Cleaning (0-100)

## Slide 9: Modeling Notes
Porous Pavement routing is performed using the Modified Puls Storage – Indication Method.
Time increments are established by the model and vary by event.
Yield reductions are due to runoff volume reduction through infiltration
The pavement surface can be any material – paver blocks, porous asphalt or concrete

## Slide 10: Modeling Notes
In Northern Climates, groundwater contamination due to Chlorides may be a problem – check with your regulatory agency
Porous pavement clogging and cleaning time frames may require a multi-year analysis to correctly evaluate performance
Clogging due to run on increases as the porous pavement area to drainage area ratio decreases
Applicable only at the source area level

## Slide 11: Surface Seepage Rate Changes to the Control Practice

## Slide 12: Surface Seepage Rate Changes to the Control Practice
Assumes 50% increase in Seepage Rate upon Cleaning

## Slide 13
Additional Output
<Filename> PPWB in SA# .csv
Available through: Tools/
Default Model Options
Water Balance File
Stage Outflow File
Surface Seepage Rate File
Detailed Output File
Stochastic Seepage Rate Detail File
Notes: Porous pavement water balance data - Lists the water surface elevation and volume data from the porous pavement device for each rainfall event.
Porous pavement stage-outflow data - Lists the discharge at each stage elevation for the seepage rate and the underdrain.
Porous pavement surface seepage rate data - Provides the change in the surface seepage rate due to gradual porous pavement clogging for each event.
Porous pavement detailed output - Hydraulic and stage data for each time increment in the model run.
Porous pavement stochastic seepage rate detail - Lists the seepage rate for each event if the random infiltration rate generator option is selected.