## Slide 1: WinSLAMM v 10 Stormwater Storage and Beneficial Uses
Using WinSLAMM v10 to Meet Urban Stormwater Management Goals

## Slide 2: We will cover . . .
References and Use
Processes
Entering Water Tank/Cistern info. into the Model

## Slide 3: Heavily Urbanized Developing Countries In Water Stressed Areas (China, India)
Most concerned with harvesting as much runoff as possible, with minimal concern related to water quality.
Not only is roof runoff harvested, but also runoff from all urban areas. Usually, all paved areas are used to harvest runoff, as maximum volumes are needed to augment the poor quality and poorly available local sources.
The water is stored in large ponds, or injected to shallow aquifers. These improve the water quality to some extent, greatly depending on the storage conditions.
Hong Kong AECOM
VISHWANATH

## Slide 4: Developing Countries With Large Rural Populations (Africa)
Most of the runoff harvesting schemes focus on collecting roof runoff for storage in tanks near homes.
The water is used for all domestic purposes and for irrigation of food subsistence crops during dry weather.
The storage tanks are therefore relatively large to provide seasonal storage.
Tanzania (Elsevier)

## Slide 5: Developed Countries With Large Urban Populations in Water Stressed Areas (Australia)
In most cases, the runoff is collected from roofs and stored in large tanks adjacent to buildings where the water is used for non-potable uses.
In some rural cases, the water is used for all domestic water uses. In large development water harvesting projects, runoff is collected from all areas and undergoes some pretreatment before storage in large (usually underground) storage tanks.
The water then undergoes very sophisticated water treatment before use. In many cases, this highly treated harvested runoff is still restricted to non-potable uses.
Heathcote, Victoria, Australia

## Slide 6: Current Stormwater Beneficial Uses in the U.S.
Many of the U.S. stormwater harvesting projects are either part of a LEED® certified project, and/or to help reduce stormwater discharges to combined sewer systems.
The collected water is not used for potable uses, but mostly for irrigation uses, and sometimes for toilet flushing or for fire suppression.
Philip Merrill Bldg. Annapolis
SMURRF, Santa Monica

## Slide 7: Irrigation Water Use
The most straight-forward beneficial use of stormwater at or near the source where the stormwater is generated is for irrigation of surrounding landscaped areas. Two approaches are:
the typical water conservation approach where minimal irrigation water (stored stormwater) is applied to make up the deficit between the evapotranspiration (ET) requirements of the landscaped plants and the soil moisture additions associated with rainfall, and
maximizing stormwater use by applying as much stormwater to the plants as they can tolerate without causing harm to the vegetation.

## Slide 8
The following table shows the monthly average rainfall for the 1973 through 1999 period at the Kansas City airport, a 26 year unbroken continuous rain record. The average total annual rainfall is typically about 37.5 inches, with most falling in the spring to early fall. A much smaller fraction of the annual rain occurs during December through February.
 | Jan | Feb | Mar | Apr | May | Jun | Jul | Aug | Sep | Oct | Nov | Dec | Total
Avg. | 1.1 | 1.2 | 2.5 | 3.4 | 5.4 | 4.2 | 4.1 | 3.6 | 4.6 | 3.3 | 2.0 | 1.6 | 37.4
COV | 0.6 | 0.5 | 0.6 | 0.6 | 0.5 | 0.4 | 0.8 | 0.6 | 0.7 | 0.8 | 0.5 | 0.8 | 0.2
Min. | 0.0 | 0.2 | 0.3 | 0.3 | 1.1 | 1.7 | 0.2 | 0.6 | 0.5 | 0.0 | 0.0 | 0.0 | 21.6
Max. | 2.8 | 2.7 | 9.0 | 8.4 | 12.4 | 8.6 | 15.4 | 9.5 | 11.1 | 10.1 | 5.1 | 5.4 | 55.2

## Slide 9
The total landscaped area in the 100 acre residential land use area is 65.1 acres, and with 576 homes, each has about 4,925 ft2 of landscaped area that could potentially be irrigated. The total annual evapotranspiration (ET) is about 52 inches a year, resulting in a rainfall deficit of about 15 inches per year.
 | in/day ET* | ET (in/month) | rainfall (in/month) | irrigation deficit (in/month) | irrigation deficit (gal/day/house)
Jan | 0.05 | 1.55 | 1.13 | 0.42 | 42
Feb | 0.10 | 2.83 | 1.24 | 1.59 | 172
Mar | 0.10 | 3.10 | 2.54 | 0.56 | 55
Apr | 0.15 | 4.50 | 3.48 | 1.02 | 104
May | 0.20 | 6.20 | 5.41 | 0.79 | 78
Jun | 0.20 | 6.00 | 4.27 | 1.73 | 177
Jul | 0.25 | 7.75 | 4.15 | 3.60 | 357
Aug | 0.25 | 7.75 | 3.63 | 4.12 | 408
Sep | 0.20 | 6.00 | 4.63 | 1.37 | 140
Oct | 0.10 | 3.10 | 3.32 | n/a | 0
Nov | 0.05 | 1.50 | 2.08 | n/a | 0
Dec | 0.05 | 1.55 | 1.60 | n/a | 0

## Slide 10
 | irrigation needs per month (gal/house) | irrigation needs per month (ft3/house) | irrigation needs per month (ft depth/house) | irrigation needs per month (inches depth/month) | irrigation needs per month (inches depth/week)
Jan | 1302 | 174 | 0.04 | 0.42 | 0.10
Feb | 4859 | 650 | 0.13 | 1.58 | 0.39
Mar | 1705 | 228 | 0.05 | 0.56 | 0.13
Apr | 3120 | 417 | 0.08 | 1.02 | 0.24
May | 2418 | 323 | 0.07 | 0.79 | 0.18
Jun | 5310 | 710 | 0.14 | 1.73 | 0.40
Jul | 11067 | 1480 | 0.30 | 3.60 | 0.81
Aug | 12648 | 1691 | 0.34 | 4.12 | 0.93
Sep | 4200 | 561 | 0.11 | 1.37 | 0.32
Oct | 0 | 0 | 0.00 | 0.00 | 0.00
Nov | 0 | 0 | 0.00 | 0.00 | 0.00
Dec | 0 | 0 | 0.00 | 0.00 | 0.00
Totals | 46629 | 6234 | 1.27 | 15.19 | 

## Slide 11: Kansas City Green Infrastructure Demonstration Project: Calculations of Water Harvesting Potential of Roof Runoff
Chart: Evapotranspiration per Month (typical turf grass)
| Jan | Feb | Mar | Apr | May | Jun | Jul | Aug | Sep | Oct | Nov | Dec
ET per month (in depth/week) | 0.35727 | 0.65231 | 0.71454 | 1.0372 | 1.4291 | 1.383 | 1.7864 | 1.7864 | 1.383 | 0.71454 | 0.34575 | 0.35727
Chart: Monthly Rainfall
| Jan | Feb | Mar | Apr | May | Jun | Jul | Aug | Sep | Oct | Nov | Dec
rainfall per month (inches/week) | 0.25516 | 0.30726 | 0.57355 | 0.812 | 1.2216 | 0.99633 | 0.9371 | 0.81968 | 1.0803 | 0.74968 | 0.48533 | 0.36129
Chart: Supplemental Irrigation Needs per Month (typical turf grass)
| Jan | Feb | Mar | Apr | May | Jun | Jul | Aug | Sep | Oct | Nov | Dec
irrigation needs per month (in depth/week) | 0.095768 | 0.39219 | 0.12541 | 0.23714 | 0.17785 | 0.40359 | 0.81403 | 0.93032 | 0.31923 | 0 | 0 | 0
Irrigation needs for the landscaped areas surrounding the homes were calculated by subtracting long-term monthly rainfall from the regional evapotranspiration demands for turf grass.

## Slide 12
Region | total roof area (%) | Landscape area (%) | ratio of roof area to landscape area | city | study period annual rain fall (in) (5-year period, 1995 to 2000) | maximum roof runoff control (%), silty soil conditions | storage tank size for max roof runoff control (ft3 storage/ft2 roof area), silty soil conditions
Central | 18.1 | 62.5 | 0.29 | Kansas City, MO | 33.46 | 90.6 | 0.72
East Coast | 15.9 | 54.5 | 0.29 | Newark, NJ | 53.01 | 61.1 | 2.00
Southeast | 8.8 | 81.1 | 0.11 | Birmingham, AL | 49.84 | 42.2 | 0.73
Southwest | 15.4 | 61.2 | 0.25 | Los Angeles, CA | 16.73 | 47.7 | 0.42
Northwest | 15.4 | 61.2 | 0.25 | Seattle, WA | 41.69 | 15.6 | 0.03
Great Lakes | 15 | 57.5 | 0.26 | Madison, WI | 28.65 | 71.7 | 0.43
Roof Runoff Harvesting Benefits for Regional Conditions. (Medium Density Residential Land Uses)

## Slide 13
For maximum use of the roof runoff to decrease runoff discharge volumes, it is possible to irrigate at the highest rate possible without causing harm to the plants. For a “healthy” lawn, total water applied (including rain) is generally about 25 mm (1 inch) of water per week, or 100 mm (4 inches) per month. Excessive watering is harmful to plants, so indiscriminate over-watering is to be avoided. Some plants can accommodate additional water. As an example, Kentucky Bluegrass, the most common lawn plant in the US, needs about 64 mm/week (2.5 in/week), or more, during the heat of the summer, and should receive some moisture during the winter.
Essex Co., NJ | Jan | Feb | Mar | Apr | May | Jun | Jul | Aug | Sep | Oct | Nov | Dec | Total Annual
Average monthly rain (in/mo) | 3.42 | 3.11 | 4.16 | 3.71 | 3.99 | 2.88 | 4.21 | 4.04 | 3.61 | 3.06 | 3.70 | 3.47 | 43.37
Lawn moisture needs (in/mo) | 2.00 | 2.00 | 4.00 | 4.00 | 8.00 | 8.00 | 10.00 | 10.00 | 10.00 | 8.00 | 4.00 | 2.00 | 72.00
Deficit irrigation need (in/mo) | 0.00 | 0.00 | 0.00 | 0.29 | 4.01 | 5.12 | 5.79 | 5.96 | 6.39 | 4.94 | 0.30 | 0.00 | 32.80
Deficit irrigation needed (gallons/day/house) 0.36 acres | 0 | 0 | 0 | 96 | 1263 | 1669 | 1826 | 1880 | 2081 | 1558 | 96 | 0 | 318,000 gal/year

## Slide 14
For maximum use of the roof runoff to decrease runoff discharged volumes, it is desired to irrigate at the highest rate possible without causing harm to the plants. Therefore, Table X8 and Figure X6 show an alternative corresponding to a possible maximum use of the roof runoff. For a “healthy” lawn, total water applied (including rain) is generally about 25 mm (1 inch) of water per week, or 100 mm (4 inches) per month. Excessive watering is harmful to plants, so indiscriminate over-watering is to be avoided. Some plants can accommodate additional water. As an example, Kentucky Bluegrass, the most common lawn plant in the US, needs about 64 mm/week (2.5 in/week), or more, during the heat of the summer, and should receive some moisture during the winter.
Chart: Inches per month
| Jan | Feb | Mar | Apr | May | Jun | Jul | Aug | Sep | Oct | Nov | Dec
Average monthly rain (in/mo) | 3.4227 | 3.1133 | 4.1598 | 3.7061 | 3.9947 | 2.8782 | 4.2094 | 4.0369 | 3.6141 | 3.0586 | 3.7041 | 3.4682
deficit for ET needs (in/mo) | 0 | 0 | 0 | 0.19392 | 0.81029 | 1.7718 | 0.59559 | 0.14814 | 0 | 0.50637 | 0 | 0
Chart: Inches per month
| Jan | Feb | Mar | Apr | May | Jun | Jul | Aug | Sep | Oct | Nov | Dec
Average monthly rain (in/mo) | 3.4227 | 3.1133 | 4.1598 | 3.7061 | 3.9947 | 2.8782 | 4.2094 | 4.0369 | 3.6141 | 3.0586 | 3.7041 | 3.4682
Deficit irrigation need (in/mo) | 0 | 0 | 0 | 0.29392 | 4.0053 | 5.1218 | 5.7906 | 5.9631 | 6.3859 | 4.9414 | 0.29588 | 0
Conservation Approach (minimum use of water):
Stormwater Management Approach (maximum use of stormwater):
Essex County, NJ, Example:

## Slide 15: Toilet Flushing Water Use
Typical domestic water use of 80 gallons per person per day (300 L per person per day) is often used for calculating residential water use (Henry and Heinke 1989).
About 45% of domestic water use is for toilet flushing, or about 35 gallons per person per day (Nat. Small Flows Clearinghouse, 1987)
Industrial water use of about 40 gallons per person per day, and commercial water use of about 25 gallons per person per day (McGhee 1991).

## Slide 16
Population densities for different land uses include (Viessmann and Hammer 1998):
  Single family residential areas: 5 to 35 persons/acre
  Multiple family residential areas: 30 to 100 persons/acre
  Apartments: 100 to 1,000 persons/acre
  Commercial areas: 15 to 30 persons/acre
  Industrial areas: 5 to 15 persons/acre
Toilet water use (Mays 2001):
  Standard toilet: 10 to 30 L/flush
  Ultra-low volume toilet: ≤6 L/flush
  Silent leaking toilet: ≥ 150 L/day
  Nonstop running toilet: ≤20 L/minute

## Slide 17
The US Census Bureau can provide population densities for any zip code in the country. That value can be used with the per capita toilet flushing water use to calculate the potential for stormwater replacement of the toilet flushing water.
A medium density residential area with 15 persons/acre and 35 gallons per day for flushing results in about 525 gallons per day per acre. Similarly, toilet use at commercial and industrial sites can be estimated using the employee numbers at the facilities (or the rough population density estimates shown above. For commercial areas with an assumed population density of 20 persons/acre and a reduced toilet use of about 20 gallons per person per day, the total toilet water use would be about 400 gallons per day per acre.
Toilet flushing water use would vary with population changes. Weekend vs. week day water use patterns are different and seasonal variations would occur due to varying workforce numbers or student populations at school or in town.

## Slide 18: Firefighting Water Volume Requirements
Firefighting water can be supplied with site stormwater runoff. Obviously, sufficient guaranteed storage is needed. The amount of water “used” for firefighting is not a continuous consumptive need for the stormwater, but the water volume needed must always be available so these volumes must be added to the storage volume for other needs.
The 2012 International Building Code (chapter 6 for types of construction) and the 2006 International Fire Code (Appendix B-5) specifies the amount of water (flow rate and duration) required for different types of buildings.

## Slide 19
As an example, a 50,000 ft2 (total floor area) type IV building (heavy timber with noncombustible external materials) would require a fire flow of 4,000 gpm (15,000 L/min) for a duration of 4 hrs. Therefore, a total volume of about 16,000 gallons (2,000 ft3), or 60m3 needs to be added to other storage volumes to provide for on-site storage of firefighting water.
Also, this volume could be exchanged frequently during large rains (draining the storage tank before the anticipated rain that would produce at least this amount of runoff volume. Additional stored stormwater can also be used during testing of firefighting systems. This can be calculated using information from the local fire marshal.

## Slide 20: Example Stormwater Beneficial Uses for a Typical House
The estimated roof runoff for a typical 2,000 ft2, 1- ½ level, house (roof area of about 1,300 ft2) would be about 40,000 gallons per year having about 50 inches of rain a year.
The total water use for this household is about 100,000 gallons per year, with the amount used for toilet flushing being about 12,000 gallons, with another 3,000 gallons used for landscaping irrigation.
For this example, the roof runoff would supply almost three times the amount of water needed for toilet flushing and landscape irrigation.

## Slide 21
January | 113 gal/day/house | July | 428
February | 243 | August | 479
March | 126 | September | 211
April | 175 | October | 71
May | 149 | November | 71
June | 248 | December | 71
The expected per household water use (gallons/day) from cisterns for toilet flushing and outside irrigation (ET deficit only) for the Kansas City study area (6 homes per acre) is:

## Slide 22: Continuous Simulations Using Long-Term Rain Records to Develop Performance Curves for Roof Runoff Storage in Tanks for Later Irrigation
Input screen for a water tank. This example screen is for a 35-gallon rain barrel, one per house (86 homes with a total roof area of 1.866 acres). The water use was calculated based on total landscaped areas and toilet flushing.

## Slide 23
Chart: Rain barrel/tank storage (ft3 per ft2 of roof area)
| 4.9735449735449824E-3 | 9.9470899470900046E-3 | 1.9894179894179988E-2 | 4.9735449735449813E-2 | 0.12433862433862462 | 0.49735449735450077
% reduction in runoff | 23.5229 | 29.4701 | 39.4114 | 56.2854 | 73.874 | 98.7722
Reductions in Annual Flow Quantity from Directly Connected Roofs with the Use of Rain Barrels and Water Tanks (Kansas City CSO Study Area)

## Slide 24
Storage per house (ft3 per ft2 of roof area) | Reduction in annual roof runoff (%) | Number of 35-gallon rain barrels for 945 ft2 roof | Tank height size required if 5 ft D (ft) | Tank height size required if 10 ft D (ft)
0.005 | 24 | 1 | 0.24 | 0.060
0.010 | 29 | 2 | 0.45 | 0.12
0.020 | 39 | 4 | 0.96 | 0.24
0.050 | 56 | 10 | 2.4 | 0.60
0.12 | 74 | 25 | 6.0 | 1.5
0.50 | 99 | 100 | 24 | 6.0
Cistern/Storage Tank Sizing vs. Performance

## Slide 25
In many areas, rainfall occurs out of synchronization with the ET requirements, requiring unusually large storage tanks, or limited performance. For other situations, the ratio of landscaped land available to irrigate was small compared to the roof areas, also leading to limited performance. In the Central and Great Lakes regions of the U.S., the greatest benefits of water storage tanks was observed, as these areas have rainfall that well match the ET deficits. In very wet (the South East or North West) areas of the U.S., performance was limited because of insufficient landscaped areas in medium density residential areas compared to roof areas to utilize most of the available roof runoff water. In the South West, the rainfall pattern was significantly out of sync with the ET deficit, also resulting in reduced benefits. In the Central and Great Lakes regions, water storage tanks of about 0.5 inches of storage can provide about 70-90% roof runoff reductions.
Conclusions

## Slide 26
If stormwater management was the goal of the water tanks, an excess amount of water could be applied to the landscaping, or even discharged to the drainage system or receiving water. Substantial amounts of water can be added to typical turf grass after a rain, without damage to the vegetation. If in a combined sewer area, the stored water in the tank can be released during periods of low flows to decrease overflows. Receiving waters can also benefit by receiving additional flows during low flow periods.